LibPSn00b Library Reference
Runtime Library v0.12b

PSn00bSDK
2018 - 2019 Meido-Tek Productions / PSn00bSDK Project

The PSn00bSDK tools and library programs fall under the terms of the Mozilla Public License. This copy of PSn00bSDK must include a copy of the Mozilla Public License, if not you must obtain a copy of this SDK with the license file intact.

As a quick summary of the Mozilla Public License; projects using MPL don’t necessarily have to be under the MPL license and source disclosure is not required, only assets that are part of PSn00bSDK must be under MPL. If any derivative modifications have been made to PSn00bSDK that improves its functionality, such changes must be committed upstream to the main repository of PSn00bSDK under the terms of the MPL. It is also the only way to ‘donate’ to the project as the PSn00bSDK project does not accept any monetary donations.

For more details on the Mozilla Public License, you can read the full license at:
https://www.mozilla.org/en-US/MPL/2.0/

PSn00bSDK is 100% free to use for both hobbyist and commercial homebrew projects. Third party distribution of PSn00bSDK is probably not advisable as libraries and tools update regularly in its current state.

PSn00bSDK Github repository:
https://github.com/Lameguy64/PSn00bSDK

# About This Manual
The purpose of this manual is to describe all available LibPSn00b library functions, macros and structures that have been implement so far throughout the development of this project. There are plans to make a LibPSn00b Library Overview companion volume that further describes the structure and purpose of the libraries of LibPSn00b but is not yet being worked on due to limited available man power of the PSn00bSDK project.
## Changes Since Last Version

Graphics Library:
- Documented DrawSyncCallback, DrawPrim and StoreImage functions.
- Documented DR_MASK, DR_TPAGE, LINE_F2, LINE_F3, LINE_F4 structures.
- Documented setDrawMask, setClut, setTPage, getClut, getTPage, setDrawTPageVal, setDrawTPage, setLineF2, setLineF3, setLineG2 and setLineG3 macros.
- Fixed documentation errors in setLineG4, InterruptCallback and DMACallback.
- Updated VsyncCallback.
## Related Documentation
Since an overview volume of the LibPSn00b Runtime Library is not yet made, the Lameguy’s PSX Programming Tutorial Series is the best available substitute for now and can be found on the Tools & Resources page of the Lameguy64 website at http://lameguy64.tk/index.php?page=tools.
The tutorial series covers both the Programmer’s Tool/PsyQ SDK and PSn00bSDK and is also essential learning materials to those new to programming for the PSX.
Note: The Lameguy64 website additionally posts updates and current developments regarding PSn00bSDK and the LibPSn00b Runtime Libraries.
Nocash’s PSX specs document may also be of great use, especially if you plan to go low level: http://problemkaputt.de/psx-spx.htm
## Documentation Credits
Lead writer: Lameguy64
# Graphics Library

## Overview
The graphics library provides functions for initializing and controlling the GPU hardware as well as various structures and macros for preparing graphics primitives to be drawn by the GPU. This library does not provide functions for 3D graphics processing, the Geometry Library (psxgte) provides such functions instead.
This library also provides a global ISR handler which other libraries depend on for handling interrupts and is installed to the kernel by ResetGraph(). Even if you don’t plan to do any graphics, it is highly recommended to call ResetGraph() at the beginning of your program.
## Structures
### DISPENV
Display environment structure
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Structure
typedef struct {
RECT	disp;	Display coordinates (framebuffer position and resolution)
RECT	screen;	Screen coordinates (picture position and size)
char	isinter;	Interlace flag (0: non-interlace, 1: interlace)
char	isrgb24;	RGB24 color mode (0: 16-bit color mode, 1: 24-bit color mode)
short	pad;	Padding
} DISPENV;
Explanation
This structure specifies the display attributes to apply to the GPU using PutDispEnv().
The disp element specifies both the offset of the framebuffer area to be displayed (disp.x, disp.y) and display resolution. Valid horizontal resolutions (for disp.w) are 256, 320, 384, 512 and 640 and vertical resolutions (for disp.h) are 240 and 480 for NTSC standard and 256 and 512 for PAL standard. The display resolution also determines the size of the rectangular area on the framebuffer to be displayed. If the display area exceeds the framebuffer area the picture would simply wrap around to the other side of the framebuffer.
Apparently the GPU is capable of outputting 272 vertical lines in PAL standard even if you have the vertical resolution set to 256. This is yet to be investigated further.
The screen element specifies the position (screen.x, screen.y) and size (screen.w, screen.h) of the picture displayed on the TV screen. A position of (0, 0) is the base position of the picture and if the picture size is set to (0, 0), default size values are used based on the resolution specified by the disp element. Specifying values that are lower or greater than the resolution specified by disp can be used to achieve custom resolutions but the hardware will not scale the pixels, it merely just crops or extends what is being shown.
The isinter flag specifies if the video signal should be interlaced. This flag must be set when using a vertical resolution of 480 or 512 pixel lines, otherwise, only the even lines would be displayed or a strange video collapse effect will occur (and no, the GPU hardware cannot output 480p at all). Interlace can be set for 240 and 256 line modes but it would introduce unnecessary jitter though it may help improve compatibility with HDTVs and video capture devices that expect an interlace jitter signal.
The isrgb24 flag specifies 24-bit true-color mode and expands the display area by 1.5x horizontally to accommodate the additional bytes needed for RGB24 pixels. This mode can’t be used for real-time graphics as the GPU only renders at 16-bit color so 24-bit mode is most useful for FMV sequences or displaying graphic illustrations from MDEC compressed image data (after decompression).
See also
PutDispEnv
### DRAWENV
Drawing environment structures
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Structure
typedef struct {
RECT	clip;	Drawing area in framebuffer within (0, 0) – (1023, 511)
short	ofs[2];	GPU drawing offset (x, y)
RECT	tw;	Initial texture page window coordinates
u_short	tpage;	Initial texture page (see getTPage())
u_char	dtd;	Dither processing (0: no dithering, 1: dithered)
u_char	dfe;	Allow drawing to displayed area (0: don’t draw to display area, 1: draw)
u_char	isbg;	Draw area clear on environment set (0: no clear, 1: clear)
u_char	r0,g0,b0;	Draw area clear color
DR_ENV	dr_env;	Drawing environment buffer (reserved)
} DRAWENV;
Explanation
This structure specifies the drawing attributes to apply to the GPU using PutDrawEnv().
The clip element specifies the rectangular area of the framebuffer that graphics primitives will be drawn to. The drawing area can be of any arbitrary size as long as it is within the framebuffer area.
The ofs[] element specifies the X,Y coordinates of the GPU offset which is the position where a coordinate of (0,0) will originate from. The coordinates specified are relative to the clip area coordinates.
The tw element specifies the texture window size and offset of the texture page. Currently that functionality is not yet implemented in PSn00bSDK so this element does nothing.
The tpage element specifies the initial texture page value to set to the GPU. A texture page can be easily calculated using getTPage() and the texture page can be changed mid-drawing using the DR_TPAGE packet.
The dtd element specifies if dither processing is enabled or not. The dither processing bit is merged with the specified texture page value and could be disabled if a DR_TPAGE primitive was processed without the dither processing bit set.
The dfe element specifies if drawing should be blocked if the area is occupied by a display area. This is normally set to zero since most page flipping setups usually draw to an area not visible to the display and is mandatory for hi-res modes as it would allow the GPU to only draw on rows that are not being displayed, allowing for a pseudo double buffered setup. Setting this to non-zero would allow drawing in a display area as well as draw on both fields in hi-res modes which might be useful for static menu screens in hi-res.
The isbg element specifies if the drawing area should be cleared when this structure is applied using PutDrawEnv(), recommended for instances where the screen is constantly being updated. The clear color is specified using the r0,g0,b0 elements.
The dr_env element is a reserved element used as a buffer by PutDrawEnv(). The DR_ENV structure can be used as a primitive packet to change the drawing environment mid-drawing for split-screen setups or off-screen render-to-texture tricks for example.
Work in progress
The tw element has no effect to the drawing environment as of version 0.09b.
See also
PutDrawEnv
### RECT
Defines a rectangular area
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	12/21/2018
Structure
typedef struct {
short	x,y;	Top left coordinates of the rectangular area
short	w,h;	Width and height of the rectangular area
} RECT;
Explanation
Used to define a rectangular area in various structures and functions.
### TIM_IMAGE
Texture Image parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	02/02/2019
Structure
typedef struct {
u_int	mode;	Image mode (bit 0-3: color depth, bit 4: CLUT flag)
RECT	*crect;	Pointer to CLUT rectangle coordinates
u_int	*caddr;	Pointer to CLUT data (or NULL if no CLUT)
RECT	*prect;	Pointer to pixel data rectangle coordinates
u_int	*paddr;	Pointer to pixel data
} TIM_IMAGE;
Explanation
Used to store texture image parameters from a TIM file with GetTimInfo. The crect, caddr, prect and paddr elements can be referenced directly to access TIM coordinates and data easily.
See also
GetTimInfo
## Structures (Primitives)
### DR_MASK
Mask mode primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	0.01b	07/17/2019
Structure
typedef struct {
u_int	tag;	Pointer to next primitive + length of this packet
u_int	code[1];	Drawing mask primitive code
} DR_MASK;
Explanation
Sets the drawing mask setting of the GPU, a limited implementation of stencil masks.
See also
setDrawMask
### DR_TPAGE
Texture page primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	07/16/2019
Structure
typedef struct {
u_int	tag;	Pointer to next primitive + length of this packet
u_int	code[1];	Texture page primitive code
} DR_TPAGE;
Explanation
A texture page primitive, used to change the current Tpage of the GPU mid-drawing.
Used alongside primitives that lack a Tpage field, such as SPRT, SPRT_8 and SPRT_16 primitives, and for setting the blend operator of untextured primitives, such as TILE, TILE_1, TILE_8, TILE_16, POLY_F3, POLY_F4, POLY_G3, and POLY_G4 primitives, that have been set for semi-transparency.
See also
setDrawTPage setDrawTPageVal
### LINE_F2, LINE_F3, LINE_F4
2-point, 3-point and 4-point solid colored line primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Structure
typedef struct {
u_int	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
} LINE_F2;

typedef struct {
u_int	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
u_int	pad;	Terminator value (usually 0x55555555)
} LINE_F3;

typedef struct {
u_int	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
short	x3,y3;	Screen coordinates 3
u_int	pad;	Terminator value (usually 0x55555555)
} LINE_F4;
Explanation
LINE_F2 draws a solid colored 2-point line between (x0, y0) – (x1, y1) with color specified by (r0, g0, b0).
LINE_F3 draws a solid colored 3-point line around (x0, y0) – (x1, y1) – (x2, y2) with color specified by (r0, g0, b0).
LINE_F4 draws a solid colored 4-point line around (x0, y0) – (x1, y1) – (x2, y2) – (x3, y3) with color specified by (r0, g0, b0).
See also
setLineF2 setLineF3 setLineF4
### LINE_G2, LINE_G3, LINE_G4
2-point, 3-point and 4-point shaded line primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Structures
typedef struct {
u_int	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 0
} LINE_G2;

typedef struct {
u_int	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,p2;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_int	pad;	Terminator value (usually 0x55555555)
} LINE_G3;

typedef struct {
u_int	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,p2;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_char	r3,g3,b3,p3;	RGB color 3 + padding
short	x3,y3;	Screen coordinates 3
u_int	pad;	Terminator value (usually 0x55555555)
} LINE_G4;
Explanation
LINE_F2 draws a solid colored 2-point line between (x0, y0) – (x1, y1) with color specified by (r0, g0, b0) –(r1, g1, b1).
LINE_F3 draws a solid colored 3-point line around (x0, y0) – (x1, y1) – (x2, y2) with color specified by (r0, g0, b0) – (r1, g1, b1) – (r2, g2, b2).
LINE_F4 draws a solid colored 4-point line around (x0, y0) – (x1, y1) – (x2, y2) – (x3, y3) with color specified by (r0, g0, b0) – (r1, g1, b1) – (r2, g2, b2) – (r3, g3, b3).
### P_TAG
Generic primitive header
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Structure
typedef struct {
u_int	addr:24;	Next primitive address
u_int	len:8;	Primitive length (in words)
u_char	r,g,b;	Primitive color
u_char	code;	Primitive code
} P_TAG;
Explanation
Normally used in various primitive preparation macros and the addPrim macro.
### POLY_F3, POLY_F4
3-point and 4-point, untextured, flat shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
} POLY_F3;

typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
short	x3,y3;	Screen coordinates 3
} POLY_F4;
Explanation
POLY_F3 draws a 3-point flat shaded, untextured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_F4 draws a 4-point flat shaded, untextured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements r0, g0, b0 specifies the color of the primitive.
Use setPolyF3 and setPolyF4 macros respectively to initialize the primitive before adding it to an ordering table.
The following figure describes the vertex order for 4-point polygons:
V0	V1

V2	V3
### POLY_FT3, POLY_FT4
3-point and 4-point, textured, flat shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad;	Padding
} POLY_FT3;

typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad0;	Padding
short	x3,y3;	Screen coordinates 3
u_char	u3,v3;	Texture coordinates 3
u_short	pad1;	Padding
} POLY_FT4;
Explanation
POLY_FT3 draws a 3-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_FT4 draws a 4-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (u0,v0), (u1,v1), (u2,v2) and (u3,v3) specify the texture coordinates within the texture page specified by tpage. Texture CLUT ID is specified by the clut element.
Elements r0, g0, b0 specifies the color of the primitive.
Use setPolyFT3 and setPolyFT4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### POLY_G3, POLY_G4
3-point and 4-point, untextured, gouraud shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
} POLY_G3;

typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,pad0;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,pad1;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_char	r3,g3,b3,pad2;	RGB color 3 + padding
short	x3,y3;	Screen coordinates 3
} POLY_G4;
Explanation
POLY_G3 draws a 3-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_G4 draws a 4-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (r0,g0,b0), (r1,g1,b1), (r2,g2,b2) and (r3,g3,b3) specifies the color of the primitive for each point.
Use setPolyG3 and setPolyG4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### POLY_GT3, POLY_GT4
3-point and 4-point, textured, gouraud shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page ID
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad2;	Padding
} POLY_GT3;

typedef struct {
u_int	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page ID
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad2;	Padding
u_char	r3,g3,b3,pad3;	RGB color 3
short	x3,y3;	Screen coordinates 3
u_char	u3,v3;	Texture coordinates 3
u_short	pad4;	Padding
} POLY_GT4;
Explanation
POLY_GT3 draws a 3-point gouraud shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_GT4 draws a 4-point gouraud shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (u0,v0), (u1,v1), (u2,v2) and (u3,v3) specify the texture coordinates within the texture page specified by tpage. Texture CLUT ID for color-index textures is specified by the clut element.
Elements (r0,g0,b0), (r1,g1,b1), (r2,g2,b2) and (r3,g3,b3) specifies the color of the primitive for each point.
Use setPolyGT3 and setPolyGT4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### SPRT
Any-size textured sprite
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	05/23/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + packet code
short	x0,y0;	Position of sprite
u_char	u0,v0;	Sprite texture coordinates within texture page. u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
u_short	w,h;	Sprite size (w must be a multiple of 2)
} SPRT;
Explanation
Draws a textured sprite primitive of any defined size, draws faster than POLY_FT4 but lacks the authority for scaling and rotation.
If you use a sprite size greater than 256x256 (or the size of the texture window), the texture will simply repeat.
Because the SPRT primitive has no element to specify a texture page, a DR_TPAGE primitive can be used to work around that limitation. In order for the primitive to be effective, it must be added to the ordering table after the SPRT primitive has been sorted and both primitives must be added to the same element of the ordering table.
Use setSprt to initialize the primitive before adding it to the ordering table.
### SPRT_8, SPRT_16
Fixed size 8 x 8 or 16 x 16 textured sprite
Library	Header	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	05/23/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + primitive code
short	x0,y0;	Position of sprite (top-left coordinates)
u_char	u0,v0;	Sprite texture coordinates within texture page, u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
} SPRT_8;

typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + primitive code
short	x0,y0;	Position of sprite (top-left coordinates)
u_char	u0,v0;	Sprite texture coordinates within texture page, u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
} SPRT_16;
Explanation
Draws a fixed size 8 x 8 or 16 x 16 pixel textured sprite, supposedly faster than SPRT.
Much like SPRT it has no texture page element so a DR_TPAGE primitive must be added to the ordering table after the SPRT primitive to specify the desired texture page value.
Use setSprt8 and setSprt16 respectively to initialize the packet before adding it to an ordering table.
### TILE
Any size flat colored sprite
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	05/23/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinate)
short	w,h;	Size of tile in pixels
} TILE;
Explanation
Draws a flat colored sprite of specified size.
Use setTile to initialize the packet before adding it to an ordering table.
### TILE_1, TILE_8, TILE_16
Fixed size 1 x 1, 8 x 8 and 16 x 16 colored sprites.
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.1b	05/23/2019
Structure
typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_1;

typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_8;

typedef struct {
u_int	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_16;
Explanation
Draws a fixed size 1 x 1, 8 x 8 or 16 x 16 flat colored sprite.
Use setTile1, setTile8, setTile16 to initialize the packet before adding it to an ordering table.
## Functions
### AddPrim
Non macro version of addPrim
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Syntax
void AddPrim(
u_int *ot,	Pointer to an ordering table element
void *p)	Pointer to a primitive packet
Explanation
Links a primitive packet to an ordering table element by setting the value from the specified table element to the primitive packet’s tag element (with the size byte retained) and the pointer to the packet is set to the specified table element.
It is recommended to generate primitive packets in a global buffer to ensure that they do not get overwritten when the GPU gets around to processing the primitive (ie. If you allocate the primitive as a local variable in a function, it may have been overwritten when the GPU gets to draw it).
A common misconception among many PS1 homebrew programmers is they sometimes believe only a single primitive packet can be added to each ordering table element. This is false because adding another primitive to an ordering table element that already has a primitive concatenates to the chain, not replace the element.
Therefore, an ordering table length of 4 to 8 elements is usually enough for purely 2D projects. Higher ordering table sizes are recommended for projects featuring 3D visuals.
See also
ClearOTagR DrawOTag
### ClearOTagR
Initializes an array to an empty ordering table (reverse order)
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	12/21/2018
Syntax
void ClearOTagR(
unsigned int *ot,	Pointer to an array to initialize into a linked list
int n)	Number of array elements
Explanation
Initializes an array of n elements specified by *ot into a linked list to use as an ordering table. An ordering table consists of an array of pointers that point from one entry to the next which primitives may be added to the chain.
This function uses DMA to clear the ordering table. It prepares a reverse order list which starts at the last entry of the array and ends at the first. This is ideal for 3D graphics as higher table entries are drawn first and lower entries are drawn last. Primitives added to one entry first are always drawn last.
To begin processing of an ordering table array initialized by this function, execute DrawOTag(ot+n-1) (draw from last entry of array) since the ordering table is initialized with pointers in reverse order.
When adding an ordering table to another ordering table using addPrims, specify the last element for p0 and the first element for p1 if the ordering table is cleared by this function.
See Also
DrawOTag
### DMACallback
Sets a callback routine for a DMA interrupt
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.10b	07/16/2019
Syntax
void *DMACallback(
int dma,	DMA channel to set callback
void (*func)())	Callback function
Explanation
Sets a callback function specified by func to a DMA channel specified by dma, executed whenever a DMA transfer for the specified channel finishes. Calling this function will automatically install a handler on IRQ3 using InterruptCallback to handle DMA interrupts.
This function is not normally exposed to programmers in the official SDK, but is made available in LibPSn00b for low-level prototyping and advanced low-level programmers. Use this function only if you know exactly what you're doing.
The following lists the hardware device associated with each DMA channel:
Channel	Device
0	MDEC input
1	MDEC output
2	GPU (used by libpsxgpu)
3	CD-ROM
4	SPU
5	PIO
6	OTC (used by libpsxgpu)
Setting a DMA callback automatically adds an interrupt callback on IRQ3 using InterruptCallback(). If a callback routine on IRQ3 has already set, DMACallback will not set its own handler.
The callback is never an interrupt handler and a callback function must be written as a normal function. Since the callback function is called within an exception handler, function must return as soon as possible. Recursive function calls must be kept a minimum due to limited stack. DMA interrupt status bits are automatically acknowledged so the callback routine does not need to acknowledge it manually.
To uninstall a callback routine, simply specify NULL or 0 for func. It will also remove the IRQ enable bit of the corresponding DMA channel. If all DMA callbacks have been removed, the DMA callback handler is removed from the ISR.
Returns
Pointer to the last installed callback routine.
### DrawOTag
Executes an ordering table
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	12/21/2018
Syntax
void DrawOTag(
u_int *ot)	Pointer to an ordering table to execute.
Explanation
Executes primitives linked into an ordering table array specified by *ot.
When executing an ordering table initialized by ClearOTagR, you must specify the last entry in the array.
DrawOTag uses DMA to query primitives to the GPU and may be non-blocking during DMA page gaps. Use DrawSync to ensure execution of the ordering table has completed.
See also
DrawSync ClearOTagR
### DrawPrim
Draws a primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Syntax
void DrawPrim(
void *pri)	Pointer to a primitives
Explanation
Draws a primitive specified by pri. Uses software I/O to send the primitive to the GPU so its not recommended for drawing all graphics.
Use only for drawing a few primitives in a very simple single buffered menu for example.
### DrawSync
Waits until all GPU drawing or VRAM transfers have completed
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	12/21/2018
Syntax
int DrawSync(
int mode)	Function mode
Explanation
Waits until the GPU has finished processing drawing commands or VRAM transfers. If mode is non-zero, returns the number of words remaining in a DMA transfer.
Work in progress
This function does not timeout if the GPU locks up due to a bad packet or corrupted ordering table as of version 0.09b.
Returns
Number of words remaining in transfer if mode = 1.
### DrawSyncCallback
Sets a callback function that is executed on drawing or VRAM transfer completion
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.10b	07/17/2019
Syntax
void *DrawSyncCallback(
void (*func)())	Pointer to a function
Explanation
Sets a callback function specified by func which will be executed on every drawing completion or VRAM transfer. Setting 0 will disable the callback.
Because the callback function is executed inside an interrupt handler, it is necessary to finish any processing as soon as possible. Sub function calls should be kept a minimum as the stack in the ISR is limited.
It is not recommended to issue VRAM or OT transfer operations within the callback function, use it only to set variables for keeping track of drawing and transfer completions.
It is recommended to define any variable manipulated by a callback function as volatile, to make sure any code reading the value will always receive changes.
See also
DrawSync
### GetInterruptCallback
Returns the address of the callback function of a specified interrupt
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.10b	06/19/2019
Syntax
void *GetInterruptCallback(
int irq)	Interrupt number
Explanation
Gets the address of the callback function of an interrupt.
Returns
Pointer to the callback function last set.
See also
InterruptCallback
### GetTimInfo
Get image parameters of a TIM image file
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	0.01b	02/02/2019
Syntax
int GetTimInfo(
unsigned int *tim,	Pointer to a TIM image file
TIM_IMAGE *timimg)	Pointer to a TIM_IMAGE structure
Explanation
Retrieves parameters from a TIM file and stores relevant values to a TIM_IMAGE structure.
Return value
0: success, 1: invalid file ID, 2: unsupported TIM version
See also
TIM_IMAGE
### GetVideoMode
Gets the current video standard mode
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	2/2/2019
Syntax
int GetVideoMode()
Explanation
Returns the current video standard mode.
Differences
Unlike the official libraries, this function returns the video mode standard currently set (ie. If this function is called on a PAL machine while in a PAL display mode, it returns 1 or MODE_PAL).
Returns
MODE_NTSC: NTSC, MODE_PAL: PAL
See also
SetVideoMode
### InterruptCallback
Sets a callback routine for an interrupt
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.10b	07/16/2019
Syntax
void *InterruptCallback(
int irq,	Interrupt number to install callback
void (*func)())	Callback function
Explanation
Sets a callback function specified by func to the ISR, which is executed whenever an interrupt specified by irq occurs. Only one callback routine can be set per interrupt number at a time.
This is a special low-level function that is not normally used by programmers in the official SDK and is usually only called internally by the libraries. It is exposed in LibPSn00b for better control over the hardware in prototyping or when performing special operations. Use this function ONLY if you know exactly what you’re doing.
The following lists the hardware device associated with each interrupt number:
Interrupt	Device
0	Vsync (used by libpsxgpu)
1	GPU (triggered only by a special GPU packet)
2	CD-ROM
3	DMA
4	Timer 0
5	Timer 1
6	Timer 2
7	Pad & Memory card
8	Serial (used by libpsxsio)
9	SPU
10	Light-gun & Expansion port
Most hardware devices would only generate an interrupt when enabled by their I/O port registers.
This function should only be called while in critical section. The ISR automatically acknowledges interrupts so the callback routine does not need to acknowledge it (except hardware devices that additionally need to be acknowledged by their I/O registers). Avoid calling too many sub functions in the callback routine as the size of the stack in the ISR is limited.
To uninstall a callback routine, simply specify NULL or 0 for func. It will also remove the IRQ mask bit of the corresponding interrupt in the IRQ hardware registers which disables the interrupt.
Returns
Pointer to the last installed callback routine.
### LoadImage
Upload image data to VRAM
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	12/21/2018
Syntax
void LoadImage(
RECT *rect,	Pointer to a RECT specifying VRAM destination coordinates
unsigned int *data)	Pointer to source image data
Explanation
Uploads image data from the source address data to VRAM. The image size and destination offset in VRAM is specified by rect using a RECT object.
LoadImage uses DMA to upload data to VRAM at high speed and could be non-blocking, use DrawSync to ensure the DMA transfer has completed. Using DrawSync when uploading multiple images at once is not necessary as LoadImage will wait for a previous transfer to complete.
If you want to upload a texture image on every frame in a real time sequence, it is best to perform the upload after a DrawSync call.
See also
DrawSync GetTimInfo
### PutDrawEnv
Applies a DRAWENV structure
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.1b	06/07/2019
Syntax
void PutDrawEnv(
DRAWENV *draw)	Pointer to a DRAWENV structures
Explanation
Applies the specified DRAWENV structure to the GPU. This function is best called when the GPU is not busy processing any primitives. Use the DrawSync function to wait for the GPU to complete processing.
Alternatively, a DR_ENV struct can be used to change the drawing environment mid-drawing.
See also
DRAWENV

### PutDispEnv
Applies a DISPENV structure
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
void PutDispEnv(
DISPENV *disp)	Pointer to a DISPENV structure
Explanation
Applies the specified DISPENV struct to the GPU. This function is best called immediately when a V-Blank occurs (using VSync) when updating the screen regularly. Use the VSync function to wait for a V-Blank to occur.
See also
DISPENV VSync
### ResetGraph
Resets the graphics subsystem
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
void ResetGraph(
int mode)	Reset mode
Explanation
Resets the GPU and graphics subsystem of libpsxgpu according to mode.
On first call, this function will additionally install its ISR subsystem to the kernel, installs its VSync callback, uninstall the BIOS CD subsystem and exit critical section regardless of mode. Because of this, it is highly recommended to call this function at the beginning of your program even if you don’t plan to do any graphics.
The following describes the behavior of the available mode numbers. The exact behavior in the official SDK is not known yet.
Mode	Operation
0	Resets the GPU entirely including video mode (default of 256x240) and sets	display mask to 0.
1	Cancels any DMA transfer and resets the GPU command buffer.
3	Resets the GPU command buffer.

### SetDefDispEnv
Sets a display environment with default parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Syntax
SetDefDispEnv(
DISPENV *disp,	Pointer to a DISPENV structure
int x, int y,	X, Y framebuffer coordinates to display
int w, int h)	Display resolution
Explanation
Prepares a DISPENV structure with the specified framebuffer and resolution coordinates using default video parameters.
The defaults are the screen element of DISPENV is set to zeroes, isinter is set 0 and isrgb24 is set 0.
See also
DISPENV PutDispEnv
### SetDefDrawEnv
Sets a drawing environment with default parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Syntax
SetDefDrawEnv(
DRAWENV *disp,	Pointer to a DRAWENV structure
int x, int y,	X, Y framebuffer coordinates to draw to
int w, int h)	Draw area size
Explanation
Prepares a DRAWENV structure with the specified framebuffer and resolution coordinates using default parameters.
The ofs[] elements of DRAWENV is set 0 (top-left), tw is set 0 (default texture window settings), tpage to 0x0a (640, 0), dtd to 1 (dithering enabled), dfe to 0 (don’t draw to displayed area), isbg to 0 (no draw area clear) and clear color values set to 0.
See also
DRAWENV PutDrawEnv
### SetDispMask
Sets the display mask
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/08/2019
Syntax
void SetDispMask(
int mask)	Display mask setting (0: no display, 1: display)
Explanation
Sets the display mask of the GPU. If mask is 0, the console will only show a black screen.
This function is useful for hiding garbage shown during video init/setup. ResetGraph automatically sets the display mask to 0.
Best called after VSync and PutDispEnv.
### SetVideoMode
Sets the video standard
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
void SetVideoMode(
int mode)	Video standard to set
Explanation
Sets the video standard by mode (MODE_NTSC for NTSC or MODE_PAL for PAL), normally used to override the video standard of the console.
Keep in mind that using a video standard other than the one specified by the region of the console will result to color problems or unstable picture without modifications, depending on the model of the console.
### StoreImage
Download image data from VRAM
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Syntax
void StoreImage(
RECT *rect,	Pointer to a RECT specifying VRAM source coordinates
unsigned int *data)	Pointer to store downloaded image data
Explanation
Downloads a portion of VRAM from an area specified by rect, and stores the downloaded pixel data to a buffer specified by data.
LoadImage uses DMA to upload data to VRAM at high speed and could be non-blocking, use DrawSync to ensure the DMA transfer has completed.
See also
DrawSync
### VSync
Wait for vertical retrace, or return elapsed vertical blank counter, or hblank count since last call
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/23/2019
Syntax
void VSync(
int mode)	Mode
Explanation
Waits until a vertical retrace occurs or returns a value using the method specified by mode, as defined below.
Mode	Operation
0	Waits until a vertical retrace event occurs.
1	Only return the Hblank count elapsed since last VSync call.
n>1	Waits until n vertical retrace events occur.
n<0	Returns number of vertical retrace events elapsed since the start of the program.
VSync() will timeout if the vertical blanking interrupt stops working either due to calling ChangeClearPAD(1), or calling _InitPad() without calling ChangeClearPAD(0) next. The function will attempt to restart vertical blanking interrupts by calling ChangeClearPAD(0) and ChangeClearRCnt(3, 0).
VSync() may also timeout if a large wait value is specified. Use a for-loop that calls VSync(0) instead to get around this limitation.
Return value
Return value varies depending on the value specified by mode.
Mode	Return value
>=0	Hblank count elapsed since last VSync call.
<0	Number of vertical retrace events elapsed since the start of your program.
See also
VSyncCallback
### VSyncCallback
Sets a specified function to be executed on every V-blank
Library	Header	Original	Introduced	Documentation Date
liblibpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
void *VsyncCallback(
void (*func)())	Pointer to a callback function
Explanation
Sets a callback function specified by func called on every V-blank. Setting 0 will disable the callback.
Because the callback function is executed during a critical section inside an ISR, it is necessary to finish any processing quickly. Sub function calls should also be kept at minimum as the stack in the ISR is limited.
It is recommended to define any variable manipulated by a callback function as volatile to make sure that any loop reading the value will always read the variable for changes.
Returns
Pointer to last callback function set.
See also
VSync
## Macros
### addPrim
Links a primitive packet to an ordering table
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
addPrim(
ot,	Pointer to an ordering table element
p)	Pointer to a primitive packet
Explanation
Links a primitive packet to an ordering table element by setting the value from the specified table element to the primitive packet’s tag element (with the size byte retained) and the pointer to the packet is set to the specified table element.
It is recommended to generate primitive packets in a global buffer to ensure that they do not get overwritten when the GPU gets around to processing the primitive (ie. If you allocate the primitive as a local variable in a function, it may have been overwritten when the GPU gets to draw it).
A common misconception among PS1 homebrew programmers is that they sometimes believe that only a single primitive packet can only be added to each ordering table element. This is false as adding another primitive to an ordering table element that already has a primitive added to it will only add to the chain, not replace it so pretty much any number of primitives can be added to a single table element. Therefore, an ordering table length of 4 to 8 elements is usually enough for a 2D game project.
See also
ClearOTagR DrawOTag
### addPrims
Links an ordering table to another ordering table
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
addPrims(
ot,	Pointer to an ordering table element
p0,	Pointer to the first element of the ordering table to add
p1)	Pointer to the last element of the ordering table to addition
Explanation
This macro links one ordering table specified by p0 and p1 to another ordering table.
The ordering table element that is considered the first element in the chain depends on which function was used to prepare the ordering table. If the ordering table was cleared using ClearOTagR the last element of the array is the first and the first element is the last, if the ordering table is cleared using ClearOTag the first element in the array is the first and the last element is the last.
See also
ClearOTagR
### getClut
Calculates and returns a CLUT value
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
getClut(
x, y)	Framebuffer coordinates to a CLUT
Explanation
Calculates a CLUT value from the specified coordinates. The resulting value is used on textured primitives with a CLUT field. x must be a multiple of 16 units, the value will be rounded down to the nearest lower multiple otherwise.
A CLUT is needed only if the texture color depth is 4-bit or 8-bit.
Primitives with a CLUT field include SPRT, SPRT_8, SPRT_16, POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
### getTPage
Calculates and returns a texture page value
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/16/2019
Syntax
getTPage(
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Blend operator mode (see below)
x, y)	Framebuffer coordinate of texture page
Explanation
Calculates a texture page value using the specified coordinates. The resulting value is used with textured primitives that have a Tpage field or a DR_TPAGE primitive (using setDrawTPageVal).
The framebuffer coordinates should be a multiple of 64 for the X axis and a multiple of 256 for the Y axis, the coordinates will be rounded down to the nearest lower multiple otherwise.
The following lists the blend modes for semi-transparent primitives (abr):
Mode	Operation
0	B:50%	+	F:50%	(50% alpha)
1	B:100%	+	F:100%	(additive)
2	B:100%	-	F:100%	(subtractive)
3	B:100%	-	F:25%	(subtract 25%)
Primitives that have a Tpage field include POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4, use DR_TPAGE and setDrawTPage or setDrawTPageVal for textured primitives without a Tpage field.
Returns
16-bit texture page value.
See also
setDrawTPage setDrawTPageVal
### setClut
Sets the CLUT field of a primitive by coordinates
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
setClut(
p,	Pointer to a primitive struct with a CLUT field
x, y)	Framebuffer coordinates to a CLUT
Explanation
Sets the CLUT field of a primitive by framebuffer coordinates. x must be a multiple of 16 pixels, the value will be rounded down to the nearest lower multiple otherwise.
Primitives with a CLUT field include SPRT, SPRT_8, SPRT_16, POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
See also
getClut
### setDrawMask
Prepares a DR_MASK primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	0.01b	07/17/2019
Syntax
setDrawMask(
p,	Pointer to a DR_MASK primitive
sb,	Set mask bit on pixels drawn (0: don’t set, 1: set)
mt)	Mask test (0: draw always, 1: don’t draw on masked pixels)
Explanation
Prepares and sets the specified values to a DR_MASK primitive. The mask feature allows for limited stencil effects with the GPU.
Setting sb to 1 makes primitives set the mask bit on every pixel drawn, the mask bit is stored on the 16th bit of each pixel within the drawing area. The mask is cleared by primitives if sb is set 0.
Textured primitives with semi-transparency bits set on either the pixels or CLUT colors of the texture will also set this mask bit regardless of the sb setting. Setting mt to 1 enables mask test, which prohibits drawing on areas that have the mask bit set in the drawing area.
The mask settings affects all GPU drawing packets as well as GPU VRAM transfer and move operations, it is recommended to issue a DR_MASK with sb:0 and mt:0 to reset the mask settings after your mask effects.
See also
DR_MASK
### setDrawTPage
Prepares a DR_TPAGE primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/16/2019
Syntax
setDrawTPage(
p,	Pointer to a DR_TPAGE primitive
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Blend operator mode (see getTPage)
x, y)	Framebuffer coordinate of texture page
Explanation
Prepares and sets the specified values to a DR_TPAGE primitive, used to change the current Tpage of the GPU mid-drawing for primitives that do not have a Tpage field, and/or to set a blending operator for semi-transparent, non-textured primitives.
The framebuffer coordinates should usually be a multiple of 64 for the X axis and a multiple of 256 for the Y axis, the coordinates will be rounded down to the nearest lower value otherwise. Texture color depth has no effect on framebuffer coordinates.
See also
DR_TPAGE
### setDrawTPageVal
Prepares a DR_TPAGE primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	Yes	0.01b	07/16/2019
Syntax
setDrawTPageVal(
p,	Pointer to a DR_TPAGE primitive
tp)	Tpage value to set (see getTPage)
Explanation
Prepares a DR_TPAGE primitive similar to setDrawTPage, but takes a single Tpage value rather than a bunch of parameters that define a Tpage.
A Tpage value is normally acquired using getTPage.
See also
DR_TPAGE
### setLineF2
Prepares a LINE_F2 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Syntax
setLineF2(
p)	Pointer to a LINE_F2 primitive
Explanation
Prepares a LINE_F2 packet by setting the appropriate packet size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineF3
Prepares a LINE_F3 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	07/16/2019
Syntax
setLineF3(
p)	Pointer to a LINE_F3 primitive
Explanation
Prepares a LINE_F4 packet by setting the appropriate packet size and code values to the primitive, and sets a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineF4
Prepares a LINE_F4 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setLineF4(
p)	Pointer to a LINE_F4 primitive
Explanation
Prepares a LINE_F4 packet by setting the appropriate packet size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineG2
Prepares a LINE_G2 primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	06/07/2019
Syntax
setLineG2(
p)	Pointer to a LINE_G2 primitive
Explanation
Prepares a LINE_G2 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setLineG3
Prepares a LINE_G3 primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	0.12b	06/07/2019
Syntax
setLineG3(
p)	Pointer to a LINE_G3 primitive
Explanation
Prepares a LINE_G3 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setLineG4
Prepares a LINE_G4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/16/2019
Syntax
setLineG4(
p)	Pointer to a LINE_G4 primitive
Explanation
Prepares a LINE_G4 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setPolyF3
Prepares a POLY_F3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyF3(
p)	Pointer to a POLY_F3 primitive
Explanation
Prepares a POLY_F3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_F3
### setPolyFT3
Prepares a POLY_FT3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyFT3(
p)	Pointer to a POLY_FT3 packet
Explanation
Prepares a POLY_FT3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_FT3
### setPolyG3
Prepares a POLY_G3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyG3(
p)	Pointer to a POLY_G3 packet
Explanation
Prepares a POLY_G3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_G3
### setPolyGT3
Prepares a POLY_GT3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyGT3(
p)	Pointer to a POLY_G3 packet
Explanation
Prepares a POLY_GT3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_GT3
### setPolyF4
Prepares a POLY_F4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyF4(
p)	Pointer to a POLY_F4 packet
Explanation
Prepares a POLY_F4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_F4
### setPolyFT4
Prepares a POLY_FT4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyFT4(
p)	Pointer to a POLY_FT4 packet
Explanation
Prepares a POLY_FT4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_FT4
### setPolyG4
Prepares a POLY_G4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyG4(
p)	Pointer to a POLY_G4 packet
Explanation
Prepares a POLY_G4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_G4
### setPolyGT4
Prepares a POLY_GT4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setPolyGT4(
p)	Pointer to a POLY_GT4 packet
Explanation
Prepares a POLY_GT4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_GT4
### setRECT
Sets coordinates to a RECT struct
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
setRECT(
v,	Pointer to a RECT struct
_x,	X coordinate to set
_y,	Y coordinate to set
_w,	Width coordinate to set
_h)	Height coordinate to set
Explanation
Sets the x, y, w, and h fields of a RECT specified by v, with coordinates specified by _x, _y, _w and _h. Cleaner looking to use over setting the fields directly.
See also
RECT
### setSprt
Prepares a SPRT primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setSprt(
p)	Pointer to a SPRT packet
Explanation
Prepares a SPRT packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y, coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT
### setSprt8
Prepares a SPRT_8 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setSprt8(
p)	Pointer to a SPRT_8 packet
Explanation
Prepares a SPRT_8 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT_8
### setSprt16
Prepares a SPRT primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setSprt16(
p)	Pointer to a SPRT_16 packet
Explanation
Prepares a SPRT_16 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT_16
### setTile
Prepares a TILE primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setTile(
p)	Pointer to a TILE packet
Explanation
Prepares a TILE packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE
### setTile1
Prepares a TILE_1 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setTile(
p)	Pointer to a TILE_1 packet
Explanation
Prepares a TILE_1 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_1
### setTile8
Prepares a TILE_8 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setTile8(
p)	Pointer to a TILE_8 packet
Explanation
Prepares a TILE_8 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_8
### setTile16
Prepares a TILE_16 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	06/07/2019
Syntax
setTile16(
p)	Pointer to a TILE_16 packet
Explanation
Prepares a TILE_16 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_16
### setTPage
Sets the Tpage of a primitive by coordinates
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
setTPage(
p,	Pointer to a primitive with a Tpage field
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Semi-transparency blend operator (see getTPage)
x, y)	Framebuffer coordinates to a texture page
Explanation
Sets the Tpage field of a primitive by coordinates.
Primitives that have a Tpage field include POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
See also
getTPage
### setVector
Sets coordinates to a VECTOR or SVECTOR struct
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	0.01b	07/17/2019
Syntax
setVector(
v,	Pointer to a VECTOR or SVECTOR struct
_x,	X coordinate to set
_y,	Y coordinate to set
_z)	Z coordinate to set
Explanation
Sets the vx, vy and vz fields of a VECTOR or SVECTOR struct specified by v, with coordinates specified by _vx, _vy and _vz. Cleaner looking to use over setting the fields directly.
# Serial Input/Output Library

## Overview
The serial library provides functions to configure and control the serial interface of the PSX. It also provides a custom device intended to replace the default tty device to direct tty output from printf() calls to the serial interface, to be viewed in a serial terminal.
The PSX’s serial interface is capable of baud rates of up to 1Mbaud but 230400 baud is the highest data rate that USB serial adapters (such as a CH340) can receive. Achieving reliable communications with high data rates is yet to be studied further.
## Functions
### _sio_control
Serial control function
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	0.10b	07/16/2019
Syntax
int _sio_control(
int cmd,	Command
int arg,	Subcommand
int param)	Parameter
Explanation
Multi-purpose serial control function, used to control and retrieve every aspect of the serial interface.
The behavior of this function varies depending on the values specified by cmd and arg.
The following describes command value combinations:
cmd	arg	Function
0	0	Read serial status register.
0	1	Read serial control register.
0	2	Read serial mode register.
0	3	Read serial baud rate.
0	4	Read 1 byte from serial interface (returns byte	received).
1	1	Set serial control register.
1	2	Set serial mode (parameters specified by param).
1	3	Set serial baud rate (value specified by param).
1	4	Write 1 byte to serial interface (byte value specified by	param).
2	0	Reset serial interface.
2	1	Acknowledge serial interrupt and comms errors.

The following describes serial control options (some values not documented in official SDK):
Bits	Definition	Description
0	CR_TXEN	TX enable.
1	CR_DTR	Output DTR signal.
2	CR_RXEN	RX enable.
3	CR_BRK	Invert TX logic levels.
4	CR_INTRST	Acknowledge IRQ and comms errors.
5	CR_RTS	Output RTS signal.
6	CR_ERRRST	Reset serial hardware.
7	Unknown (always 0).
8-9	Interrupt when RX buffer has n bytes.
CR_BUFSIZ_1	00: Interrupt on 1 byte.
CR_BUFSIZ_2	01: Interrupt on 2 bytes.
CR_BUFSIZ_4	10: Interrupt on 4 bytes.
CR_BUFSIZ_8	11: Interrupt on 8 bytes.
10	CR_TXIEN	Interrupt on TX ready.
11	CR_RXIEN	Interrupt on RX receive.
12	CR_DSRIEN	Interrupt on DSR signal.
13-15	Unused (always zero).
The following describes serial mode options:
Bits	Definition	Description
0-1	None	Baud rate reload factor (must be 0x2 always).
2-3	Character length.
MR_CHLEN_5	00: 5 bits per word.
MR_CHLEN_6	01: 6 bits per word.
MR_CHLEN_7	10: 7 bits per word.
MR_CHLEN_8	11: 8 bits per word.
4	MR_PEN	Parity enable.
5	MR_P_EVEN	Odd parity (definition is misleading).
6-7	Stop bit length.
MR_SB_01	01: 1 stop bit.
MR_SB_10	10: 1.5 stop bits.
MR_SB_11	11: 2 stop bits.
8-15	Unused (always zero).
The following describes serial status bits:
Bits	Definition	Description
0	SR_TXRDY	TX ready.
1	SR_RXRDY	Bytes pending in RX buffer.
2	SR_TXU	TX completed.
3	SR_PERROR	Parity error.
4	SR_OE	RX buffer overflow.
5	SE_FE	RX bad stop bit.
6	RX input level.
7	SR_DSR	DSR signal level.
8	SR_CTS	CTS signal level.
9	SR_IRQ	Interrupt request.
10	Unknown (always zero).
11-25	15-bit baud rate timer.
### AddSIO
Installs a serial tty device
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	0.10b	06/14/2019
Syntax
void AddSIO(
int baud)	Baud rate.
Explanation
Replaces the default BIOS tty device (and Caetla’s tty device) with a serial tty device which redirects all stdout output (such as printf) to serial. The data rate is specified by baud, the rest of the parameters are 8 data bits, 1 stop bit, no parity and no hardware handshake by default.
This function can be called at the very beginning of your program (even before ResetGraph) to receive every printf message in your program.
### DelSIO
Deletes the serial tty device
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	0.10b	06/14/2019
Syntax
void DelSIO(void)
Explanation
Deletes the serial tty device, not recommended as any further tty output will likely crash the system.
### WaitSIO
Waits for serial
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	Yes	0.10b	06/14/2019
Syntax
void WaitSIO(void)
Explanation
Waits until a single byte is received from the serial interface, intended to be called immediately after AddSIO and is useful for pausing your program so you can open a terminal program and receive all tty messages.
### Sio1Callback
Sets a serial callback routine
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	0.10b	06/14/2019
Syntax
void *Sio1Callback(
void (*func)(void))	Callback function.
Explanation
Sets a function specified by func as a callback routine that is executed whenever the serial interface generates an interrupt enabled by CR_TXIEN, CR_RXIEN or CR_DSRIEN using _sio_control(1, 1, <param>). If func is zero, the callback is disabled.
It is recommended to read at least 1 byte from the serial interface and call _sio_control(2, 1, 0) to acknowledge the serial interrupt at the end of your callback routine.
Since the callback function is executed in the global ISR, sub function calls must be kept at minimum due to limited stack available. The callback function must return as soon as possible to avoid missing any further interrupt requests.
Return value
Address of previously set callback function.