LibPSn00b Library Reference
Draft: March 25, 2022

PSn00bSDK
2018 - 2022 Meido-Tek Productions / PSn00bSDK Project

The PSn00bSDK tools and library programs fall under the terms of the Mozilla Public License. This copy of PSn00bSDK must include a copy of the Mozilla Public License, if not you must obtain a copy of this SDK with the license file intact.

As a quick summary of the Mozilla Public License; projects using MPL don’t necessarily have to be under the MPL license and source disclosure is not required, only assets that are part of PSn00bSDK must be under MPL. If any derivative modifications have been made to PSn00bSDK that improves its functionality, such changes must be committed upstream to the main repository of PSn00bSDK under the terms of the MPL. It is also the only way to ‘donate’ to the project as the PSn00bSDK project does not accept any monetary donations.

For more details on the Mozilla Public License, you can read the full license at:
https://www.mozilla.org/en-US/MPL/2.0/

PSn00bSDK is 100% free to use for both hobbyist and commercial homebrew projects. Third party distribution of PSn00bSDK is probably not advisable as libraries and tools update regularly in its current state.

PSn00bSDK Github repository:
https://github.com/Lameguy64/PSn00bSDK

# About This Manual
The purpose of this manual is to describe all available LibPSn00b library functions, macros and structures that have been implement so far throughout the development of this project.
There are some plans to make a LibPSn00b Library Overview companion volume that further describes the structure, use and purpose of the libraries of LibPSn00b but is not yet being worked on due to limited available man power of the PSn00bSDK project as of the writing of this document.
## Related Documentation
Since an overview volume of the LibPSn00b Runtime Library is not yet made, the Lameguy’s PSX Programming Tutorial Series is the best available substitute document for beginners alike for now. This can be found on the Tools & Resources page of the Lameguy64 website at http://lameguy64.net/index.php?page=tools.
The tutorial series covers both the Programmer’s Tool/PsyQ SDK and PSn00bSDK and is also essential learning materials to those new to programming for the PSX.
Note: The Lameguy64 website additionally posts updates and current developments regarding PSn00bSDK and the LibPSn00b Runtime Libraries on occasion.
Nocash’s PSX specs document may also be of great use, especially if you plan to go low level: http://problemkaputt.de/psx-spx.htm
## Documentation Credits
Lead writer: Lameguy64
# CD-ROM Library

## Overview
The LibPSn00b CD-ROM library provides facilities for using the CD-ROM hardware of the PS1. Unlike the CD-ROM library of the official SDK, the LibPSn00b CD-ROM library is immune to the 30 file and directory limit and is capable of parsing directories containing as many files as the ISO9660 file system can support, unless the records are too large to be loaded into the PS1’s memory. However, to maintain compatibility with the PS1 BIOS, the root directory must not exceed the 30 file limit and the entire disc should contain no more than 45 directories total, otherwise the disc will be unbootable to the console.
Whilst the CD-ROM library is not constrained by the 30 file per directory limit, it does not support Joliet CD-ROM extensions to support long file names. However, a library extension is considered for future development.
### Library Status
As of July 25, 2020, the state of the LibPSn00b CD-ROM library is as follows:
Feature	Status
CD-ROM Control	Fully Working
CD-ROM Track Query	Fully Working
CD-Audio Playback	Fully Working
CD-XA Audio Playback	Fully Working
Data Reading	Mostly working (see CdGetSector)
ISO9660 File System Support	Fully Working
STR Data Streaming	Not yet implemented, but possible with own implementation.
Multi-session Support	Fully Working (not automatic, see CdLoadSession)

## Structures
### CdlATV
CD-ROM attenuation parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Structure
typedef struct CdlATV
{
u_char	val0;	CD to SPU L-to-L volume
u_char	val1;	CD to SPU L-to-R volume
u_char	val2;	CD to SPU R-to-R volume
u_char	val3;	CD to SPU R-to-L volume
} CdlATV;
Explanation
This structure specifies parameters for the CD-ROM attenuation. Values must be of range 0 to 127.
The CD-ROM attenuation can be used to set the CD-ROM audio output to mono (0x40, 0x40, 0x40, 0x40) or reversed stereo (0x00, 0x80, 0x00, 0x80). It can also be used to play one of two stereo channels to both speakers.
The CD-ROM attenuation affects CD-DA and CD-XA audio.
See also
CdMix
### CdlDIR
CD-ROM directory query context handle
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	Yes	R56	02/28/2020
Structure
typedef void* CdlDIR;
Explanation
Used to store a directory context created by CdOpenDir(). An open context can then be used with CdReadDir() and closed with CdCloseDir().
See Also
CdOpenDir
### CdlFILE
File entry structure
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Structure
typedef struct CdlFILE
{
CdlLOC	loc;	CD-ROM position coordinates of file
u_long	size;	Size of file in bytes
char	name[16];	File name
} CdlFILE;
Explanation
Used to store basic information of a file such as logical block location and size. Currently, CdSearchFile() is the only function that uses this struct but it will be used in directory listing functions that may be implemented in the future.
See also
CdSearchFile
### CdlFILTER
Structure used to set CD-ROM XA filter
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/19/2019
Structure
typedef struct CdlFILTER
{
u_char	file;	File number to fetch (usually 1)
u_char	chan;	Channel number (0 through 7)
u_short	pad;	Padding
} CdlFILTER;
Explanation
This structure is used to specify stream filter parameters for CD-ROM XA audio streaming using the CdlSetfilter command. This only affects CD-ROM XA audio streaming.
CD-ROM XA audio is normally comprised of up to 8 or more ADPCM compressed audio streams interleaved into one continuous stream of data. The data stream is normally read at 2x speed but only one of eight XA audio streams can be played at a time. The XA stream to play is specified by the CdlSetfilter command and this struct.
The CD-ROM XA filter can be changed during CD-ROM XA audio playback with zero audio interruption. This can be used to achieve dynamic music effects by switching to alternate versions of a theme to fit specific scenes seamlessly.
See also
CdControl
### CdlLOC
CD-ROM positional coordinates
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Structure
typedef struct CdlLOC
{
u_char	minute;	Minutes (BCD)
u_char	second;	Seconds (BCD)
u_char	sector;	Sector or frame (BCD)
u_char	track;	Track number (not used)
} CdlLOC;
Explanation
This structure is used to specify CD-ROM positional coordinates for CdlSetloc, CdlReadN and CdlReadS CD-ROM commands. Use CdIntToPos() to set parameters from a logical sector number.
See also
CdIntToPos CdControl
## Functions
### CdAutoPauseCallback
Sets a callback function for auto pause
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	Yes	R45	12/18/2019
Syntax
long *CdAutoPauseCallback(
void(*func)())	Callback function
Explanation
The callback function specified in *func is executed when an auto pause interrupt occurs when the current CD-ROM mode is set with CdlModeAP. Auto pause interrupt occurs when CD Audio playback reaches the end of the audio track. Specifying 0 disables the callback.
This can be used to easily loop CD audio automatically without requiring any intervention in your software loop.
Returns
Pointer to the last callback function set.	Zero if no callback was set previously.
See Also
CdControl
### CdCloseDir
Closes a directory context created by CdOpenDir().
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	Yes	R56	02/28/2020
Syntax
void CdCloseDir(
CdlDIR	*dir)	Directory context
Explanation
Closes a directory query context created by CdOpenDir().
Behavior is undefined when closing a previously closed directory context.
See also
CdOpenDir
### CdControl
Issues a control command to the CD-ROM controller
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/12/2019
Syntax
int CdControl(
u_char	com,	Command value
u_char	*param,	Command parameters
u_char	*result)	Pointer of buffer to store result
Description
Sends a CD-ROM command specified by com to the CD-ROM controller, waits for an acknowledge interrupt (very fast) then returns. It will also issue parameters from param to the CD-ROM controller if the command accepts parameters. Response data from the CD-ROM controller is stored to result on commands that produce response data.
Because this function waits for an acknowledge interrupt from the CD-ROM controller, this function should not be used in a callback. Instead, use CdControlF().
Commands that are blocking require the use of CdSync() to wait for the command to fully complete.
CD-ROM Control Commands:
Command	Value	Parameter	Blocking	Description
CdlNop	0x01	-	No	Also known as Getstat. Normally used	to query the CD-ROM status, which is	retrieved using CdStatus().
CdlSetloc	0x02	CdlLOC	No	Sets the seek target location, but	does not perform a seek. Actual	seeking begins upon issuing	CdlSeekL, CdlSeekP, CdlPlay,	CdlReadN and CdlReadS	commands.
CdlPlay	0x03	u_char	No	Begins CD Audio playback. CD-ROM	mode must be set with CdlModeDA	and CdlSetMode flags to work	properly. CdlModeAP flag enables	automatic pause at end of track.	Parameter specifies an optional track	number to play (Note: some	emulators do not support the track	parameter).
CdlForward	0x04	-	No	Fast forward (CD Audio only),	issue CdlPlay to stop fast forward.
CdlBackward	0x05	-	No	Rewind (CD Audio only), issue	CdlPlay to stop rewind.
CdlReadN	0x06	CdlLOC	No	Begin reading data sectors. Used in	conjunction with CdReadCallback().
CdlStandby	0x07	-	Yes	Also known as MotorOn, starts CD	motor and remains idle.
Command	Value	Parameter	Blocking	Description
CdlStop	0x08	-	Yes	Stops playback and the disc	itself.
CdlPause	0x09	-	Yes	Stops playback or data reading,	but leaves the disc on standby.
CdlInit	0x0A	-	Yes	Initialize the CD-ROM controller.
CdlMute	0x0B	-	No	Mutes CD audio (both DA and XA).
CdlDemute	0x0C	-	No	Unmutes CD audio (both DA and XA).
CdlSetfilter	0x0D	CdlFILTER	No	Set XA audio filter.
CdlSetmode	0x0E	u_char	No	Set CD-ROM mode.
CdlGetparam	0x0F	-	No	Returns current CD-ROM mode and	file/channel filter settings.
CdlGetlocL	0x10	-	No	Returns current logical CD position,	mode and XA filter parameters.
CdlGetlocP	0x11	-	No	Returns current physical CD position	(using SubQ location data).
CdlSetsession (orig)	0x12	u_char	Yes	Seek to specified session on a	multi-session disc.
CdlGetTN	0x13	-	No	Get CD-ROM track count.
CdlGetTD	0x14	u_char	No	Get specified track position.
CdlSeekL	0x15	-	Yes	Logical seek to target position, set by	last CdlSetloc command.
CdlSeekP	0x16	-	Yes	Physical seek to target position, set	by last CdlSetloc command.
CdlTest (orig)	0x19	varies	Yes	Special test command not disclosed	to official developers (see nocash	documents for more info).
CdlReadS	0x1B	CdlLOC	No	Begin reading data sectors without	pausing for error correction.
CD-ROM Return Values:
Command	0	1	2	3	4	5	6	7
CdlGetparam	stat	mode	0	file	channel	-	-	-
CdlGetlocL	amin	asec	aframe	mode	file	channel	sm	ci
CdlGetlocP	track	index	min	sec	frame	amin	asec	aframe
CdlGetTN	stat	first	last	-	-	-	-	-
CdlGetTD	stat	min	sec	-	-	-	-	-
Note: Values are in BCD format.
Returns
1 if the command was issued successfully. Otherwise 0 if a previously issued command has not yet finished processing.
See also
CdSync CdControlF btoi itob
### CdControlB
Issues a CD-ROM command to the CD-ROM controller (non-blocking)
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdControlB(
u_char	com,	Command value
u_char	*param,	Command parameters
u_char	*result)	Pointer of buffer to store result
Explanation
This function works just like CdControl(), but blocks on blocking commands until said blocking command has completed.
Because this function waits for an acknowledge interrupt from the CD-ROM controller, this function should not be used in a callback. Use CdControlF() instead.
See also
CdControl CdControlF
### CdControlF
Issues a CD-ROM command to the CD-ROM controller (does not block)
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/19/2019
Syntax
int CdControlF(
u_char	com,	Command value
u_char	*param)	Command parameters
Explanation
This function works more or less the same as CdControl() but it does not block even for the acknowledge interrupt from the CD-ROM controller. Since this function is non-blocking it can be used in a callback function.
When using this function in a callback, a maximum of two commands can be issued at once and only the first command can have parameters. This is because the CD-ROM controller can only queue up to two commands and the parameter FIFO is not cleared until the last command is acknowledged. But waiting for acknowledgment in a callback is not possible.
See also
CdControl
### CdGetToc
Get CD-ROM TOC information
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdGetToc(
CdlLOC	*toc)	Pointer to an array of CdlLOC entries
Explanation
Retrieves the track entries from a CD’s table of contents (TOC). The function can return up to 99 track entries, which is the maximum number of audio tracks the CD standard supports.
This function only retrieve the minutes and seconds of an audio track’s position as the CD-ROM controller only returns the minutes and seconds of a track, which may result in the end of the previous track being played instead of the intended track to be played. This can be remedied by having a 2 second pregap on each audio track on your disc.
Returns
Number of tracks on the disc, zero on error.
See also
CdControl
### CdGetSector
Get data from the CD-ROM sector buffered
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	03/25/2022
Syntax
int CdGetSector(
void	*madr,	Pointer to memory buffer to store sector data
int	size)	Number of 32-bit words to retrieve
Explanation
Reads sector data that is pending in the CD-ROM sector buffer and stores it to *madr. Uses DMA to transfer the sector data and blocks very briefly until said transfer completes.
This function is intended to be called within a callback routine set using CdReadyCallback() to fetch read data sectors from the CD-ROM sector buffer.
Returns
Always 1.
See also
CdReadyCallback
### CdMode
Gets the last CD-ROM mode
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdMode(void)
Explanation
Returns the CD-ROM mode last set when issuing a CdlSetmode command. The function returns instantly as it merely returns a value stored in an internal variable.
Since the value is simply a copy of what was specified from the last CdlSetmode command, the mode value may become inaccurate if CdlInit or other commands that affect the CD-ROM mode have been issued previously.
Returns
Last CD-ROM mode value.
### CdMix
Set CD-ROM mixer or attenuation
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdMix(
CdlATV	*vol)	CD-ROM attenuation parameters.
Explanation
Sets the CD-ROM attenuation parameters from a CdlATV struct specified by vol. The CD-ROM attenuation settings are different from the SPU CD-ROM volume.
Normally used to configure CD and XA audio playback for mono or reverse stereo output, though this was rarely used in practice.
Returns
Always 1.
See also
CdlATV
### CdPosToInt
Translates CD-ROM positional coordinates to a logical sector number
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdPosToInt(
CdlLOC *p)	Pointer to a CdlLOC struct.
Explanation
Translates the CD-ROM position parameters from a CdlLOC struct specified by p to a logical sector number. The translation takes the lead-in offset of 150 sectors into account so the logical sector number returned would begin at zero.
Returns
Logical sector number minus the 150 sector lead-in.
### CdIntToPos
Translates a logical sector number to CD-ROM positional coordinates
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
CdlLOC *CdIntToPos(
int	i,	Logical sector number
CdlLOC	*p)	Pointer to a CdlLOC structure
Explanation
This function translates the logical sector number from i to CD-ROM positional coordinates stored to a CdlLOC struct specified by p. The translation takes the lead-in offset into account so the first logical sector begins at 0 and the result will be offset by 150 sectors.
Returns
Pointer to the specified CdlLOC struct plus 150 sectors.
### CdInit
Initializes the CD-ROM library
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/12/2019
Syntax
int CdInit(
int	mode)	Reserved (may be used in the future)
Description
Initializes the CD-ROM subsystem which includes hooking the required IRQ handler, sets up internal variables of the CD-ROM library and attempts to initialize the CD-ROM controller. The mode parameter does nothing but may be used in future updates of this library.
This function must be called after ResetGraph and before any other CD-ROM library function that interfaces with the CD-ROM controller. This function may not be called twice as it may cause instability or would just crash.
Returns
Always 1. May change in the future.
### CdIsoError
Retrieve CD-ROM ISO9660 parser status
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	Yes	R57	02/18/2020
Syntax
int CdIsoError()
Explanation
Returns the status of the file system parser from the last call of a file system related function, such as CdSearchFile(), CdGetVolumeLabel() and CdOpenDir(). Use this function to retrieve the exact error occurred when either of those functions fail.
Returns
CD-ROM ISO9660 parser error code, as listed below.
Value	Description
CdlIsoOkay	File system parser okay.

CdlIsoSeekError	Logical seek error occurred. May occur when attempting to query the file	system while an Audio CD is inserted, which does not contain a file system.

CdlIsoReadError	Read error occurred while reading the CD-ROM file system descriptor.

CdlIsoInvalidFs	Disc does not contain a standard ISO9660 file system.
CdlIsoLidOpen	Lid is open when attempting to parse the CD-ROM file system.
### CdLoadSession
Locates and parses the specified disc session
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	Yes	R66	07/18/2020
Syntax
int CdLoadSession(
int session)	Session number (1 = first session)
Explanation
Loads a session specified by session on a multi-session disc. Uses CdlSetsession to seek to the specified disc session, then scans the following 512 sectors for an ISO volume descriptor. If a volume descriptor is found the file system of that session is parsed and files inside the new session can be accessed using regular CD-ROM file and directory querying functions (CdSearchFile(), CdOpenDir(), CdReadDir(), CdCloseDir()). No special consideration is required when reading files from a new session.
Loading a session takes 5-10 seconds to complete depending on the distance between the beginning of the disc and the start of the specified session. If the session specified does not exist, the disc will stop and would take 15-20 seconds to restart. The function does not support loading the most recent session of a disc automatically due to limitations of the CD-ROM hardware, so the user must be prompted to specify which session to load and to keep a record of the number of sessions that have been written to the disc.
This function can also be used to update the Table of Contents (TOC) and reparse the file system regardless of the media change status by simply loading the first session. This is most useful for accessing files or audio tracks on a disc that was inserted using the swap trick method (it is recommended to stop the disc using CdlStop then restart it with CdlStandby after a button prompt for convenience, if you wish to implement this capability). Seeking to sessions other than the first session does not work with the swap trick however, so a chipped or unlockable console is desired for reading multi-session discs.
Notes
When the lid has been opened, the current CD-ROM session is reset to the first session on the disc.
The console may produce an audible click sound when executing this function. This is normal, and the click sound is no different to the click heard on disc spin-up in older models of the console.
Returns
Returns zero on success. On failure due to open lid, bad session number or no volume descriptor found in specified session, returns -1 and return value of CdIsoError() is updated.
### CdOpenDir
Open a directory on the CD-ROM file system
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	Yes	R56	02/28/2020
Syntax
CdlDIR* CdOpenDir(
const char*	path)	Directory path to open.
Explanation
Opens a directory on the CD-ROM file system to read the contents of a directory.
A path name must use the backslash character (\) as the directory name separator (in C/C++, you must use double backslash as backslash is used to specify special characters in strings such as \n). The path must be absolute and should begin with a backslash character. It should also not be prefixed with a device name (ie. \MYDIR1\MYDIR2 will work but not cdrom:\MYDIR1\MYDIR2).
The file system routines in libpsxcd can query directory paths of up to 128 characters.
The ISO9660 file system routines of libpsxcd does not support long file names as it only supports the original file descriptor format (no Rock Ridge or Joliet extensions) that only supports MS-DOS style 8.3 file names, even though the file system specification supports longer names.
Returns
Pointer of a CdlDIR context, NULL if an error occurred.
See also
CdReadDir CdCloseDir
### CdRead
Read sectors from the CD-ROM
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	06/07/2021
Syntax
int CdRead(
int	sectors,	Number of sectors to read
u_long	*buf,	Pointer to buffer to store sectors read
int	mode)	CD-ROM mode for reading
Explanation
Reads a number sectors specified by sectors from the location set by the last CdlSetloc command, the read sectors are then stored to a buffer specified by buf. mode specifies the CD-ROM mode to use for the read operation.
The size of the sector varies depending on the sector read mode specified by mode. For standard data sectors it is multiples of 2048 bytes. If CdlModeSize0 is specified the sector size is 2328 bytes which includes the whole sector minus sync, adress, mode and sub header bytes. CdlModeSize1 makes the sector size 2340 which is the entire sector minus sync bytes.
Ideally, CdlModeSpeed must be specified to read data sectors at double CD-ROM speed.
This function blocks very briefly to issue the necessary commands to start CD-ROM reading. To determine if reading has completed use CdReadSync or CdReadCallback.
Returns
Always returns 0 even on errors. This may change in future versions.
See also
CdReadSync CdReadCallback
### CdReadCallback
Sets a callback function for read completion
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	06/07/2021
Syntax
u_long CdReadCallback(
CdlCB	func)	Callback function

void (*func)(int status,	CD-ROM status
u_char *result)	Pointer to a result buffer
Explanation
Works much the same as CdSyncCallback() but for CdRead(). Sets a callback with the specified function func. The callback is executed whenever a read operation initiated by CdRead() has completed.
status is the CD-ROM status from the command that has completed processing. *result points to a read result buffer.
See also
CdRead
### CdReadDir
Read a directory entry from an open directory context
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R56	02/28/2020
Syntax
int	CdReadDir(
CdlDIR	*dir,	Open directory context (from CdOpenDir())
CdlFILE	*file)	Pointer to a CdlFILE struct
Explanation
Retrieves a file entry from an open directory context and stores it to a CdlFILE struct specified by file. Repeated calls of this function retrieves the next directory entry available until there are no more directory entries that follow.
Returns
1 if there are proceeding directory entries that follow, otherwise 0.
See also
CdOpenDir
### CdReadSync
Waits for CD-ROM read completion or returns read status
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/19/2019
Syntax
int CdReadSync(
int	mode,	Mode
u_char	*result)	Pointer to store most recent CD-ROM status
Explanation
This function works more or less like CdSync() but for CdRead(). If mode is zero the function blocks if CdRead() was issued earlier until reading has completed. If mode is non-zero the function completes immediately and returns number of sectors remaining.
A buffer specified by result will be set with the most recent CD-ROM status value from the last read issued.
Returns
Number of sectors remaining. If reading is completed, 0 is returned. On error, -1 is returned.
See also
CdRead
### CdReadyCallback
Sets a callback function
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	03/25/2022
Syntax
long CdReadyCallback(
CdlCB	func)	Callback function

void (*func)(int status,	CD-ROM status
u_char *result)	Pointer to a result buffer
Explanation
Sets a callback with the specified function func. The callback is executed whenever there’s an incoming data sector from the CD-ROM controller during CdlReadN or CdlReadS. The pending sector data can be retrieved using CdGetSector().
status is the CD-ROM status code from the last CD command that has finished processing. *result corresponds to the result pointer that was passed by the last CdControl()/CdControlB() call.
This callback cannot be used in conjunction with CdRead() because it also uses this callback hook for its own internal use. The previously set callback is restored after read completion however.
Returns
Pointer to last callback function set.
See also
CdControl CdControlB CdGetSector
### CdSearchFile
Locates a file in the CD-ROM file system
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/19/2019
Syntax
CdlFILE *CdSearchFile(
CdlFILE	*loc,	Pointer to a CdlLOC struct to store file information
const char	*filename)	Path and name of file to locate
Explanation
Searches a file specified by filename by path and name in the CD-ROM file system and returns information of the file if found. The file information acquired will be stored to loc.
Directories must be separated with backslashes (\) and a leading backslash is optional and paths must reference from the root directory. File version identifier (;1) at the end of the file name is also optional. File and directory names are case insensitive.
The ISO9660 file system routines of libpsxcd does not support long file names as it only supports the original file descriptor format, which is limited to MS-DOS style 8.3 file names.
Upon calling this function for the first time, the ISO descriptor of the disc is read and the whole path table is cached into memory. Next the directory descriptor of the particular directory specified is loaded and cached to locate the file specified. The directory descriptor is kept in memory as long as the consecutive files to be searched are stored in the same directory until a file in another directory is to be searched. On which the directory descriptor is unloaded and a new directory descriptor is read from the disc and cached. Therefore, locating files in the same directory is faster as the relevant directory descriptor is already in memory and no disc reads are issued.
As of Revision 66 of PSn00bSDK, media change is detected by checking the CD-ROM lid open status bit and attempting to acknowledge it with a CdlNop command, to discriminate the status from an open lid or changed disc.
Returns
Pointer to the specified CdlFILE struct. Otherwise NULL is returned when the file is not found.
### CdStatus
Get the most recent CD-ROM status
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
int CdStatus(void)
Explanation
Returns the CD-ROM status since the last command issued. The status value is updated by most CD-ROM commands.
To get the current CD-ROM status you can issue CdlNop commands at regular intervals to update the CD-ROM status this function returns.
Returns
CD-ROM status from last comand issued.
See also
CdControl
### CdSync
Wait for blocking command or blocking status
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/18/2019
Syntax
int CdSync(
int	mode,	Mode
u_char	*result)	Pointer to store most recent CD-ROM status
Explanation
If mode is zero the function blocks if a blocking command was issued earlier until the command has finished. If mode is non-zero the function returns a command status value.
A buffer specified by result will be set with the most recent CD-ROM status value from the last command issued.
Returns
Command status is returned as one of the following definitions:
CdlComplete	Command completed.
CdlNoIntr	No interrupt, command busy.
CdlDiskError	CD-ROM error occurred.
See also
CdControl
### CdSyncCallback
Sets a callback function
Library	Header File	Original	Introduced	Documentation Date
libpsxcd	psxcd.h	No	R45	12/18/2019
Syntax
u_long CdSyncCallback(
CdlCB	func)	Callback function

void (*func)(int status,	CD-ROM status
u_char *result)	Pointer to a result buffer
Explanation
Sets a callback with the specified function func. The callback is executed whenever a blocking command has completed.
status is the CD-ROM status from the command that has completed processing. *result corresponds to the *result parameter on CdControl()/CdControlB() and returns the pointer to the buffer last set with that function.
Returns
Pointer to last callback function set.
See also
CdControl CdControlB CdSync
## Macros
### btoi
Translates a BCD format value to decimal
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
btoi(
b)	BCD format value
Explanation
Translates a specified value in BCD format (ie. 32/0x20 = 20) into a decimal integer, as the CD-ROM controller returns integer values only in BCD format.
### itob
Translates a decimal value to BCD
Library	Header File	Original	Introduced	Documentation Date
libpsxcd.a	psxcd.h	No	R45	12/18/2019
Syntax
itob(
i)	Decimal value
Explanation
Translates a decimal integer into a BCD format value (ie. 20 = 32/0x20), as the CD-ROM controller only accepts values in BCD format.
# Geometry Library

## Overview
The Geometry Transformation Engine, often referred to as the GTE, is most responsible for providing 3D capabilities to the PS1. This is effectively an all-integer math co-processor connected directly to the CPU, as it is accessed using COP2 and related MIPS instructions to access registers and issue commands to the GTE.
## GTE Register Summary
### Data Registers
To access these registers, use MIPS opcodes mfc2, mtc2, lwc2 and swc2 or relevant C macros.
Name	Register Number	Format	Description
C2_VXY0	$0	Vector 0 (X, Y, Z)
C2_VZ0	$1
C2_VXY1	$2	Vector 1 (X, Y, Z)
C2_VZ1	$3
C2_VXY2	$4	Vector 2 (X, Y, Z)
C2_VZ2	$5
C2_RGB	$6	24-bit Color + Primitive Code
C2_OTZ	$7	Average Z
C2_IR0	$8	Accumulator (interpolation)
C2_IR1	$9	Accumulator (vector)
C2_IR2	$10
C2_IR3	$11
C2_SXY0	$12	Screen XY coordinate FIFO (3 levels)
C2_SXY1	$13
C2_SXY2	$14
C2_SXYP	$15	Screen XY projection result
C2_SZ0	$16	Screen Z coordinate FIFO (4 levels)
C2_SZ1	$17
C2_SZ2	$18
C2_SZ3	$19
C2_RGB0	$20	RGB value output FIFO (4 levels)
C2_RGB1	$21
C2_RGB2	$22
C2_MAC0	$24	32-bit Accumulator (value)
C2_MAC1	$25	32-bit Accumulator (vector)
C2_MAC2	$26
C2_MAC3	$27
C2_IRGB	$28	RGB conversion (48-bit to 15-bit)
C2_ORGB	$29
C2_LZCS	$30	Count leading zeros/leading ones
C2_LZCR	$31
### Control Registers
To access these registers, use MIPS opcodes cfc2 and ctc2 or relevant C macros.
Name	Register Number	Description
C2_R11R12	$0	16-bit rotation matrix (1,1), (1,2)
C2_R13R21	$1	16-bit rotation matrix (1,3), (2,1)
C2_R22R23	$2	16-bit rotation matrix (2,2), (2,3)
C2_R31R32	$3	16-bit rotation matrix (3,1), (3,2)
C2_R33	$4	16-bit rotation matrix (3,3)
C2_TRX	$5	Translation Vector (X)
C2_TRY	$6	Translation Vector (Y)
C2_TRZ	$7	Translation Vector (Z)
C2_L11L12	$8	16-bit light source matrix (1,1), (1,2)
C2_L13L21	$9	16-bit light source matrix (1,3), (2,1)
C2_L22L23	$10	16-bit light source matrix (2,2), (2,3)
C2_L31L32	$11	16-bit light source matrix (3,1), (3,2)
C2_L33	$12	16-bit light source matrix (3,3)
C2_RBK	$13	Back color (Red)
C2_GBK	$14	Back color (Green)
C2_BBK	$15	Back color (Blue)
C2_LR1LR2	$16	16-bit light color matrix (R1,R2)
C2_LR3LG1	$17	16-bit light color matrix (R3,G1)
C2_LG2LG3	$18	16-bit light color matrix (G2,G3)
C2_LB1LB2	$19	16-bit light color matrix (B1,B2)
C2_LB3	$20	16-bit light color matrix (B3)
C2_RFC	$21	Fog far color (Red)
C2_GFC	$22	Fog far color (Green)
C2_BFC	$23	Fog far color (Blue)
C2_OFX	$24	GTE projection X offset
C2_OFY	$25	GTE projection Y offset
C2_H	$26	Projection plane distance (FOV)
C2_DQA	$27	Depth queuing coefficient
C2_DQB	$28	Depth queuing offset
C2_ZSF3	$29	gte_avsz3() divisor factor
C2_ZSF4	$30	gte_avsz4() divisor factor
C2_FLAG	$31	Calculation flags
## Macros (GTE Registers)
### gte_ldv0 gte_ldv1 gte_ldv2
Loads a single SVECTOR to individual GTE vector registers (inline assembly macro)
Library	Header File	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/18/2020
Syntax
gte_ldv0(
v0 )	Pointer to an SVECTOR

gte_ldv1(
v0 )	Pointer to an SVECTOR

gte_ldv2(
v0 )	Pointer to an SVECTOR
Explanation
Loads values from an SVECTOR struct to GTE data registers C2_VXY0-2 and C2_VZ0-2.
### gte_ldv3
Load three SVECTORs to GTE vector registers at once (inline assembly macro)
Library	Header File	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/18/2020
Syntax
gte_ldv3(
r0,	Pointer to first SVECTOR
r1,	Pointer to second SVECTOR
r2 )	Pointer to third SVECTOR
Explanation
Loads values from three SVECTOR structs to GTE data registers C2_VXY0 and C2_VZ0, C2_VXY1 and C2_VZ1, C2_VXY2 and C2_VZ2 at once.
### gte_ldrgb
Load a CVECTOR to GTE register C2_RGBC (inline assembly macro)
Library	Header File	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_ldrgb(
r0 )	Pointer to a CVECTOR structure
Explanation
Loads a CVECTOR value to GTE data register C2_RGBC.
The primitive code (the last byte of a CVECTOR) is passed to the color FIFO registers when performing lighting compute operations, so it can be stored to the RGBC field of a primitive directly without any additional operation required.
### gte_ldopv2
Loads three 32-bit values to GTE registers C2_IR1, C2_IR2 and C2_IR3 (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_ldopv2(
r0,	Pointer to first 32-bit value to load
r1,	Pointer to second 32-bit value to load
r2 )	Pointer to third 32-bit value to load
Explanation
Loads three 32-bit values to GTE data registers C2_IR1, C2_IR2 and C2_IR3.
### gte_SetGeomOffset
Sets the GTE screen offset (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetGeomOffset(
r0,	Screen X offset in pixel units
r1 )	Screen Y offset in pixel units
Explanation
Sets the values of the GTE screen offset which is applied to 2D projected coordinates when performing perspective transformation.
The values are set to GTE control registers C2_OFX and C2_OFY.
### gte_SetGeomScreen
Sets the distance of the projection plane (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetGeomScreen(
r0 )	Projection plane distance
Explanation
Sets the specified value to GTE control register C2_H which determines the projection plane distance, otherwise known as the field of view.
### gte_SetTransMatrix
Sets the translation portion of a MATRIX to the GTE (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetTransMatrix(
r0 )	Pointer to a MATRIX
Explanation
Sets the translation coordinates from a MATRIX struct to GTE control registers C2_TRX, C2_TRY and C2_TRZ respectively.
### gte_SetRotMatrix
Sets a 3x3 rotation matrix portion from a MATRIX to the GTE (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetRotMatrix(
r0 )	Pointer to a MATRIX
Explanation
Sets the 3x3 rotation matrix coordinates from a MATRIX struct to GTE control registers C2_R11R12, C2_R13R21, C2_R22R23, C2_R31R32 and C2_R33.
### gte_SetLightMatrix
Sets a 3x3 lighting matrix from a MATRIX to the GTE (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetRotMatrix(
r0 )	Pointer to a MATRIX
Explanation
Sets the 3x3 lighting matrix coordinates from a MATRIX struct to GTE control registers C2_L11L12, C2_L13L21, C2_L22L23, C2_L31L32 and C2_L33.
The lighting matrix is essentially a triplet of three light direction vectors. L11, L12 and L13 represents the X, Y and Z coordinates of light source 0 for example. Coordinates must be normalized to ensure correct results.
### gte_SetColorMatrix
Sets a 3x3 color matrix from a MATRIX to the GTE (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetColorMatrix(
r0 )	Pointer to a MATRIX
Explanation
Sets the 3x3 color matrix values from a MATRIX struct to GTE control registers C2_LR1LR2, C2_LR3LG1, C2_LG2LG3, C2_LB1LB2 and C2_LB3.
The light color matrix is essentially a triplet of three RGB colors for each of the three light sources. LR1, LG1 and LB1 represents the R, G and B color values for light source 0 for example. Values are of range 0 to 4095, higher values will be saturated.
### gte_SetBackColor
Sets an RGB color value to the GTE (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_SetBackColor(
r0,	Value for red
r1,	Value for green
r2 )	Value for blue
Explanation
Sets the specified RGB value to GTE control registers C2_RBK, C2_GBK and C2_BBK. This specifies the color value to use when a normal faces away from the direction of the light source. This can be considered as the ambient light color.
## Macros (GTE Commands)
### gte_avsz3
Average screen Z result (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	12/03/2020
Syntax
gte_avsz3()	5 cycles
Explanation
Averages the values of GTE registers C2_SZ1, C2_SZ2 and C2_SZ3, multiplies it by C2_ZSF3 and divides the result by 0x1000 before storing to C2_OTZ. Used to compute the ordering table depth level for a three-vertex primitive.
The following equation is performed when executing this GTE command:
MAC0 = ZSF3*(SZ1+SZ2+SZ3)
OTZ = MAC0/1000h
### gte_avsz4
Average screen Z result (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	12/03/2020
Syntax
gte_avsz4()	6 cycles
Explanation
Averages the values of GTE registers C2_SZ1, C2_SZ2, C2_SZ3 and C2_SZ4, multiplies it by C2_ZSF4 and divides the result by 0x1000 before storing to C2_OTZ. Used to compute the ordering table depth level for a four-vertex primitive.
The following equation is performed when executing this GTE command:
MAC0 = ZSF4*(SZ1+SZ2+SZ3+SZ4)
OTZ = MAC0/1000h
### gte_nclip
Normal clipping (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_nclip()	8 cycles
Explanation
Computes the sign of three screen coordinates (C2_SXY0-3) used for backface culling. If the value of C2_MAC0 is negative, the coordinates are inverted and thus the triangle is back facing.
The following equation is performed when executing this GTE command:
MAC0 = SX0*SY1 + SX1*SY2 + SX2*SY0 - SX0*SY2 - SX1*SY0 – SX2*SY1
### gte_rtps
Rotate, Translate and Perspective Single (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_rtps()	15 cycles
Explanation
Performs rotation, translation and perspective calculation of a single vertex. Divide overflows are simply saturated allowing for crude Z clipping. Check C2_FLAG to determine which overflow error has occurred during calculation.
The following equation is performed when executing this GTE command:
IR1 = MAC1 = (TRX*4096 + R11*VX0 + R12*VY0 + R13*VZ0) >> 12
IR2 = MAC2 = (TRY*4096 + R21*VX0 + R22*VY0 + R23*VZ0) >> 12
IR3 = MAC3 = (TRZ*4096 + R31*VX0 + R32*VY0 + R33*VZ0) >> 12
SZ3 = MAC3
MAC0=(((H*131072/SZ3)+1)/2)*IR1+OFX, SX2=MAC0/65536 MAC0=(((H*131072/SZ3)+1)/2)*IR2+OFY, SY2=MAC0/65536 MAC0=(((H*131072/SZ3)+1)/2)*DQA+DQB, IR0=MAC0/4096
### gte_rtpt
Rotate, Translate and Perspective Triple (inline assembly macro)
Library	Header	Original	Introduced	Documentation Date
-	inline_c.h	No	R1	09/24/2020
Syntax
gte_rtps()	23 cycles
Explanation
Performs rotation, translation and perspective calculation of three vertices at once.
The equation performed is the same as gte_rtps() only repeated three times for each vertex. The result of the first vertex is stored in GTE data register C2_SXY0, the second vector in C2_SXY1 then C2_SXY2.
## Functions
### ApplyMatrixLV
Multiply vector by matrix
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
VECTOR *ApplyMatrixLV(
MATRIX *m,	Input matrix
VECTOR *v0,	Input vector
VECTOR *v1)	Output vector
Explanation
Multiplies vector v0 with matrix m, result is stored to v1. Replaces the current GTE rotation matrix and translation vector with m.
Often used to calculate a translation vector in relation to the rotation matrix for first person or vector camera perspectives (see “fpscam” example).
Return Value
Pointer to v1.
### CompMatrixLV
Composite coordinate matrix transform
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
VECTOR *CompMatrixLV(
MATRIX *v0,	Input matrix A
MATRIX *v1,	Input matrix B
MATRIX *v2)	Output matrix
Explanation
Performs vector multiply by matrix with vector addition from v0 to the translation vector of v1. Then, multiples the rotation matrix of v0 by the rotation matrix of v1. The result of both operations is then stored in v2. Replaces the current GTE rotation matrix and translation vector with v0.
Often used to adjust the matrix (includes rotation and translation) of an object relative to a world matrix, so the object would render relative to the world matrix (ie. the bouncing cube in the “fpscam” example).
Return Value
Pointer to v2.
### hicos
Get a value of cos (integer, high precision version)
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
int hicos(
int a)	Angle in degrees (131072 = 360 degrees)
Explanation
Returns the cos value of angle a.
Return Value
Cosine value (4096 = 1.0).
### hisin
Get a value of sin (integer, high precision version)
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
int hisin(
int a)	Angle in degrees (131072 = 360 degrees)
Explanation
Returns the sin value of angle a.
Return Value
Sine value (4096 = 1.0).
### icos
Get a value of cos (integer)
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
int icos(
int a)	Angle in degrees (4096 = 360 degrees)
Explanation
Returns the cos value of angle a.
Uses Taylor series all-integer sine implementation that is both small and fast, does not use a lookup table.
Return Value
Cosine value (4096 = 1.0).
### isin
Get a value of sin (integer)
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
int isin(
int a)	Angle in degrees (4096 = 360 degrees)
Explanation
Returns the sine value of angle a.
Uses Taylor series all-integer sine implementation that is both small and fast, does not use a lookup table.
Return Value
Sine value (4096 = 1.0).
### PushMatrix
Pushes the current GTE matrix to the matrix stack
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
void PushMatrix(void)
Explanation
Pushes the current GTE rotation matrix and translation vector to the internal matrix stack.
Only one matrix stack level is currently supported.
### PopMatrix
Pops the last matrix pushed into the matrix stack back to the GTE
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
void PopMatrix(void)
Explanation
Pops the last inserted matrix in the internal matrix stack back to the GTE.
Only one matrix stack level is currently supported.
### RotMatrix
Defines the rotation matrix of a MATRIX
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
MATRIX *RotMatrix(
SVECTOR *r,	Rotation vector (input)
MATRIX *m)	Matrix (output)
Explanation
Defines the rotation matrix of m from rotation coordinates of r.
The rotation order of each axis of SVECTOR is X,Y,Z as described in the equation below.
s1 = sin( vx )~s2 = sin( vy )~s3 = sin( vz ) newline c1 = cos( vx )~c2 = cos( vy )~c3 = cos( vz ) newline newline mX = left lbrace matrix { 1.0#0#0##0#c1#-s1##0#s1#c1 } right rbrace~ mY = left lbrace matrix { c2#0#s2##0#1.0#0##-s2#0#c2 } right rbrace~ mZ = left lbrace matrix { c3#-s3#0##s3#c3#0##0#0#1.0 } right rbrace newline newline m = ( mX * mY * mZ )
Keep in mind that all matrix operations are performed in fixed point integer math with 12-bit fractions, where 4096 equals to a floating point value of 1.0.
Return value
Pointer to m.
See also
gte_SetRotMatrix
### Square0
Calculates the square of a VECTOR
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
void Square0(
VECTOR *v0,	Input vector
VECTOR *v1)	Output vector
Explanation
Calculates the square of vector v0 and stores the result to v1.
### TransMatrix
Defines the translation vector of a MATRIX
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
MATRIX *TransMatrix(
MATRIX *m,	Translation vector (input)
VECTOR *r)	Matrix (output)
Explanation
Simply sets the translation vector of MATRIX m. To perform accumulative translation operations, see CompMatrixLV.
Return value
Pointer to m.
See also
RotMatrix CompMatrixLV gte_SetTransMatrix
### VectorNormalS
Normalizes a VECTOR into SVECTOR format
Library	Header File	Original	Introduced	Documentation Date
libpsxgte.a	psxgte.h	No	R1	12/03/2020
Syntax
void VectorNormalS(
VECTOR *v0,	Input (raw) 32-bit vector
SVECTOR *v1)	Output (normalized) 16-bit vector
Explanation
Normalizes a 32-bit vector into a 16-bit vector with 12-bit fractions (4096 = 1.0, 2048 = 0.5).
# Graphics Library

## Overview
The graphics library provides functions for initializing and controlling the GPU hardware as well as various structures and macros for preparing graphics primitives to be drawn by the GPU. This library does not provide functions for 3D graphics processing, the Geometry Library (psxgte) provides such functions instead.
This library also provides a global ISR handler which other libraries depend on for handling interrupts and is installed to the kernel by ResetGraph(). Even if you don’t plan to do any graphics, it is highly recommended to call ResetGraph() at the beginning of your program.
### Library Status
As of September 12, 2020, the state of the LibPSn00b GPU library is as follows:
Feature	Status
GPU Initialization	Fully Working
Interrupt Service Subsystem	Fully Working
Video Standard Select	Fully Working
Primitives	Mostly Implemented
Ordering Tables	Fully Implemented
DMA VRAM Upload/Download	Fully Working
DMA Ordering Table Transfer	Fully Working
DMA Ordering Table Clear	Fully Working
VSync/DrawSync Callbacks	Fully Working
## Structures
### DISPENV
Display environment structure
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Structure
typedef struct _DISPENV {
RECT	disp;	Display coordinates (framebuffer position and resolution)
RECT	screen;	Screen coordinates (picture position and size)
char	isinter;	Interlace flag (0: non-interlace, 1: interlace)
char	isrgb24;	RGB24 color mode (0: 16-bit color mode, 1: 24-bit color mode)
short	pad;	Padding
} DISPENV;
Explanation
This structure specifies the display attributes to apply to the GPU using PutDispEnv().
The disp element specifies both the offset of the framebuffer area to be displayed (disp.x, disp.y) and display resolution. Valid horizontal resolutions (for disp.w) are 256, 320, 384, 512 and 640 and vertical resolutions (for disp.h) are 240 and 480 for NTSC standard and 256 and 512 for PAL standard. The display resolution also determines the size of the rectangular area on the framebuffer to be displayed. If the display area exceeds the framebuffer area the picture would simply wrap around to the other side of the framebuffer.
Apparently the GPU is capable of outputting 272 vertical lines in PAL standard even if you have the vertical resolution set to 256. This is yet to be investigated further.
The screen element specifies the position (screen.x, screen.y) and size (screen.w, screen.h) of the picture displayed on the TV screen. A position of (0, 0) is the base position of the picture and if the picture size is set to (0, 0), default size values are used based on the resolution specified by the disp element. Specifying values that are lower or greater than the resolution specified by disp can be used to achieve custom resolutions but the hardware will not scale the pixels, it merely just crops or extends what is being shown.
The isinter flag specifies if the video signal should be interlaced. This flag must be set when using a vertical resolution of 480 or 512 pixel lines, otherwise, only the even lines would be displayed or a strange video collapse effect will occur (the GPU hardware is not capable of 480p output at all). Interlace can be set for 240 and 256 line modes but it introduces unnecessary jitter, though it improves compatibility with some HDTVs and video capture devices that expect an interlace jitter signal. You may consider this as an option if you wish to implement HDTV compatibility options in your project.
The isrgb24 flag specifies 24-bit true-color mode and expands the display area on the framebuffer by 1.5x horizontally to accommodate the additional bytes needed for RGB24 pixels. This mode cannot be used for real-time graphics as the GPU only renders at 16-bit color, so 24-bit mode is most useful for FMV sequences, or displaying graphic illustrations from MDEC compressed image data (after decompression).
See also
PutDispEnv
### DRAWENV
Drawing environment structures
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Structure
typedef struct _DRAWENV {
RECT	clip;	Drawing area in framebuffer within (0, 0) – (1023, 511)
short	ofs[2];	GPU drawing offset (x, y)
RECT	tw;	Initial texture page window coordinates
u_short	tpage;	Initial texture page (see getTPage())
u_char	dtd;	Dither processing (0: no dithering, 1: dithered)
u_char	dfe;	Allow drawing to displayed area (0: don’t draw to display area, 1: draw)
u_char	isbg;	Draw area clear on environment set (0: no clear, 1: clear)
u_char	r0,g0,b0;	Draw area clear color
DR_ENV	dr_env;	Drawing environment buffer (reserved)
} DRAWENV;
Explanation
This structure specifies the drawing attributes to apply to the GPU using PutDrawEnv().
The clip element specifies the rectangular area of the framebuffer that graphics primitives will be drawn to. The drawing area can be of any arbitrary size as long as it is within the framebuffer area.
The ofs[] element specifies the X,Y coordinates of the GPU offset which is the position where a coordinate of (0,0) will originate from. The coordinates specified are relative to the clip area coordinates.
The tw element specifies the texture window size and offset of the texture page. Currently that functionality is not yet implemented in PSn00bSDK so this element does nothing.
The tpage element specifies the initial texture page value to set to the GPU. A texture page can be easily calculated using getTPage() and the texture page can be changed mid-drawing using the DR_TPAGE packet.
The dtd element specifies if dither processing is enabled or not. The dither processing bit is merged with the specified texture page value and could be disabled if a DR_TPAGE primitive was processed without the dither processing bit set.
The dfe element specifies if drawing should be blocked if the area is occupied by a display area. This is normally set to zero since most page flipping setups usually draw to an area not visible to the display and is mandatory for hi-res modes as it would allow the GPU to only draw on rows that are not being displayed, allowing for a pseudo double buffered setup. Setting this to non-zero would allow drawing in a display area as well as draw on both fields in hi-res modes which might be useful for static menu screens in hi-res.
The isbg element specifies if the drawing area should be cleared when this structure is applied using PutDrawEnv(), recommended for instances where the screen is constantly being updated. The clear color is specified using the r0,g0,b0 elements.
The dr_env element is a reserved element used as a buffer by PutDrawEnv(). The DR_ENV structure can be used as a primitive packet to change the drawing environment mid-drawing for split-screen setups or off-screen render-to-texture tricks for example.
Work in progress
The tw element has no effect to the drawing environment as of version 0.09b.
See also
PutDrawEnv
### RECT
Defines a rectangular area
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	12/21/2018
Structure
typedef struct _RECT {
short	x,y;	Top left coordinates of the rectangular area
short	w,h;	Width and height of the rectangular area
} RECT;
Explanation
Used to define a rectangular area in various structures and functions.
### TIM_IMAGE
Texture Image parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _TIM_IMAGE {
u_long	mode;	Image mode (bit 0-3: color depth, bit 4: CLUT flag)
RECT	*crect;	Pointer to CLUT rectangle coordinates
u_long	*caddr;	Pointer to CLUT data (or NULL if no CLUT)
RECT	*prect;	Pointer to pixel data rectangle coordinates
u_long	*paddr;	Pointer to pixel data
} TIM_IMAGE;
Explanation
Used to store texture image parameters from a TIM file with GetTimInfo. The crect, caddr, prect and paddr elements can be referenced directly to access TIM coordinates and data easily.
See also
GetTimInfo
## Structures (Primitives)
### DR_AREA
Drawing area primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R32	01/14/2022
Structure
typedef struct DR_AREA {
u_long	tag;	Pointer to next primitive + length of packet
u_long	code[2];	Primitive code
} DR_AREA;
Explanation
Changes the current drawing area in similar function to using DRAWENV and SetDefDrawEnv, but can be inserted as a primitive packet allowing to change the drawing area mid-rendering.
See Also
setDrawArea
### DR_MASK
Mask mode primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	R1	06/07/2021
Structure
typedef struct _DR_MASK {
u_long	tag;	Pointer to next primitive + length of packet
u_long	code[1];	Drawing mask primitive code
} DR_MASK;
Explanation
Sets the drawing mask setting of the GPU, a limited implementation of stencil masks.
See also
setDrawMask
### DR_OFFSET
Drawing offset primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R32	01/14/2022
Structure
typedef struct _DR_OFFSET
{
u_long	tag;	Pointer to next primitive + length of packet
u_long	code[1];	Primitive code
} DR_OFFSET;
Explanation
Sets the current drawing offset for graphics primitives. Often used in tandem with DR_AREA to update the drawing offset.
See Also
setDrawOffset
### DR_TPAGE
Texture page primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _DR_TPAGE {
u_long	tag;	Pointer to next primitive + length of packet
u_long	code[1];	Texture page primitive code
} DR_TPAGE;
Explanation
A texture page primitive, used to change the current Tpage of the GPU mid-drawing.
Used alongside primitives that lack a Tpage field, such as SPRT, SPRT_8 and SPRT_16 primitives, and for setting the blend operator of untextured primitives, such as TILE, TILE_1, TILE_8, TILE_16, POLY_F3, POLY_F4, POLY_G3, and POLY_G4 primitives, that have been set for semi-transparency.
See also
setDrawTPage setDrawTPageVal
### DR_TWIN
Texture window primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R32	01/14/2022
Structure
typedef struct _DR_TWIN
{
u_long	tag;	Pointer to next primitive + length of packet
u_long	code[2];	Primitive code
} DR_TWIN;
Explanation
Sets texture page window parameters. A texture window is used to restrict textured primitives to a small region of a texture page to allow for wrapping textures.
See Also
setTexWindow
### LINE_F2, LINE_F3, LINE_F4
2-point, 3-point and 4-point solid colored line primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _LINE_F2 {
u_long	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
} LINE_F2;

typedef struct _LINE_F3 {
u_long	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
u_long	pad;	Terminator value (usually 0x55555555)
} LINE_F3;

typedef struct _LINE_F4 {
u_long	tag;	Pointer to next primitive + length of this packet
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
short	x3,y3;	Screen coordinates 3
u_long	pad;	Terminator value (usually 0x55555555)
} LINE_F4;
Explanation
LINE_F2 draws a solid colored 2-point line between (x0, y0) – (x1, y1) with color specified by (r0, g0, b0).
LINE_F3 draws a solid colored 3-point line around (x0, y0) – (x1, y1) – (x2, y2) with color specified by (r0, g0, b0).
LINE_F4 draws a solid colored 4-point line around (x0, y0) – (x1, y1) – (x2, y2) – (x3, y3) with color specified by (r0, g0, b0).
See also
setLineF2 setLineF3 setLineF4
### LINE_G2, LINE_G3, LINE_G4
2-point, 3-point and 4-point shaded line primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structures
typedef struct _LINE_G2 {
u_long	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 0
} LINE_G2;

typedef struct _LINE_G3 {
u_long	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,p2;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_long	pad;	Terminator value (usually 0x55555555)
} LINE_G3;

typedef struct _LINE_G4 {
u_long	tag;	Pointer to next primitive + length of packet
u_char	r0,g0,b0,code;	RGB color 0 + primitive code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,p1;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,p2;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_char	r3,g3,b3,p3;	RGB color 3 + padding
short	x3,y3;	Screen coordinates 3
u_long	pad;	Terminator value (usually 0x55555555)
} LINE_G4;
Explanation
LINE_F2 draws a solid colored 2-point line between (x0, y0) – (x1, y1) with color specified by (r0, g0, b0) –(r1, g1, b1).
LINE_F3 draws a solid colored 3-point line around (x0, y0) – (x1, y1) – (x2, y2) with color specified by (r0, g0, b0) – (r1, g1, b1) – (r2, g2, b2).
LINE_F4 draws a solid colored 4-point line around (x0, y0) – (x1, y1) – (x2, y2) – (x3, y3) with color specified by (r0, g0, b0) – (r1, g1, b1) – (r2, g2, b2) – (r3, g3, b3).
See Also
setLineG2 setLineG3 setLineG4
### P_TAG
Generic primitive header
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _P_TAG {
u_long	addr:24;	Next primitive address
u_long	len:8;	Primitive length (in words)
u_char	r,g,b;	Primitive color
u_char	code;	Primitive code
} P_TAG;
Explanation
Normally used in various primitive preparation macros and the addPrim macro.
### POLY_F3, POLY_F4
3-point and 4-point, untextured, flat shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _POLY_F3 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
} POLY_F3;

typedef struct _POLY_F4 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
short	x1,y1;	Screen coordinates 1
short	x2,y2;	Screen coordinates 2
short	x3,y3;	Screen coordinates 3
} POLY_F4;
Explanation
POLY_F3 draws a 3-point flat shaded, untextured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_F4 draws a 4-point flat shaded, untextured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements r0, g0, b0 specifies the color of the primitive.
Use setPolyF3 and setPolyF4 macros respectively to initialize the primitive before adding it to an ordering table.
The following figure describes the vertex order for 4-point polygons:
V0	V1

V2	V3
### POLY_FT3, POLY_FT4
3-point and 4-point, textured, flat shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _POLY_FT3 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad;	Padding
} POLY_FT3;

typedef struct _POLY_FT4 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color + primitive code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad0;	Padding
short	x3,y3;	Screen coordinates 3
u_char	u3,v3;	Texture coordinates 3
u_short	pad1;	Padding
} POLY_FT4;
Explanation
POLY_FT3 draws a 3-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_FT4 draws a 4-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (u0,v0), (u1,v1), (u2,v2) and (u3,v3) specify the texture coordinates within the texture page specified by tpage. Texture CLUT ID is specified by the clut element.
Elements r0, g0, b0 specifies the color of the primitive.
Use setPolyFT3 and setPolyFT4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### POLY_G3, POLY_G4
3-point and 4-point, untextured, gouraud shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _POLY_G3 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
} POLY_G3;

typedef struct _POLY_G4 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	r1,g1,b1,pad0;	RGB color 1 + padding
short	x1,y1;	Screen coordinates 1
u_char	r2,g2,b2,pad1;	RGB color 2 + padding
short	x2,y2;	Screen coordinates 2
u_char	r3,g3,b3,pad2;	RGB color 3 + padding
short	x3,y3;	Screen coordinates 3
} POLY_G4;
Explanation
POLY_G3 draws a 3-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_G4 draws a 4-point flat shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (r0,g0,b0), (r1,g1,b1), (r2,g2,b2) and (r3,g3,b3) specifies the color of the primitive for each point.
Use setPolyG3 and setPolyG4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### POLY_GT3, POLY_GT4
3-point and 4-point, textured, gouraud shaded polygon primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _POLY_GT3 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page ID
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad2;	Padding
} POLY_GT3;

typedef struct _POLY_GT4 {
u_long	tag;	Pointer tag to primitive + packet length
u_char	r0,g0,b0,code;	RGB color 0 + code
short	x0,y0;	Screen coordinates 0
u_char	u0,v0;	Texture coordinates 0
u_short	clut;	Texture CLUT ID
u_char	r1,g1,b1,pad0;	RGB color 1
short	x1,y1;	Screen coordinates 1
u_char	u1,v1;	Texture coordinates 1
u_short	tpage;	Texture page ID
u_char	r2,g2,b2,pad1;	RGB color 2
short	x2,y2;	Screen coordinates 2
u_char	u2,v2;	Texture coordinates 2
u_short	pad2;	Padding
u_char	r3,g3,b3,pad3;	RGB color 3
short	x3,y3;	Screen coordinates 3
u_char	u3,v3;	Texture coordinates 3
u_short	pad4;	Padding
} POLY_GT4;
Explanation
POLY_GT3 draws a 3-point gouraud shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2).
POLY_GT4 draws a 4-point gouraud shaded, textured polygon to screen coordinates (x0,y0) – (x1,y1) – (x2,y2) – (x3,y3).
Elements (u0,v0), (u1,v1), (u2,v2) and (u3,v3) specify the texture coordinates within the texture page specified by tpage. Texture CLUT ID for color-index textures is specified by the clut element.
Elements (r0,g0,b0), (r1,g1,b1), (r2,g2,b2) and (r3,g3,b3) specifies the color of the primitive for each point.
Use setPolyGT3 and setPolyGT4 macros respectively to initialize the primitive before adding it to an ordering table.
See POLY_F3, POLY_F4 for a visual figure of the vertex order for 4-point polygons.
### SPRT
Any-size textured sprite
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _SPRT {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + packet code
short	x0,y0;	Position of sprite
u_char	u0,v0;	Sprite texture coordinates within texture page. u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
u_short	w,h;	Sprite size (w must be a multiple of 2)
} SPRT;
Explanation
Draws a textured sprite primitive of any defined size, draws faster than POLY_FT4 but lacks the authority for scaling and rotation.
If you use a sprite size greater than 256x256 (or the size of the texture window), the texture will simply repeat.
Because the SPRT primitive has no element to specify a texture page, a DR_TPAGE primitive can be used to work around that limitation. In order for the primitive to be effective, it must be added to the ordering table after the SPRT primitive has been sorted and both primitives must be added to the same element of the ordering table.
Use setSprt to initialize the primitive before adding it to the ordering table.
### SPRT_8, SPRT_16
Fixed size 8 x 8 or 16 x 16 textured sprite
Library	Header	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _SPRT_8 {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + primitive code
short	x0,y0;	Position of sprite (top-left coordinates)
u_char	u0,v0;	Sprite texture coordinates within texture page, u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
} SPRT_8;

typedef struct _SPRT_16 {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of sprite + primitive code
short	x0,y0;	Position of sprite (top-left coordinates)
u_char	u0,v0;	Sprite texture coordinates within texture page, u0 must be a multiple of 2
u_short	clut;	Sprite texture CLUT ID (see getClut)
} SPRT_16;
Explanation
Draws a fixed size 8 x 8 or 16 x 16 pixel textured sprite, supposedly faster than SPRT.
Much like SPRT it has no texture page element so a DR_TPAGE primitive must be added to the ordering table after the SPRT primitive to specify the desired texture page value.
Use setSprt8 and setSprt16 respectively to initialize the packet before adding it to an ordering table.
### TILE
Any size flat colored sprite
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _TILE {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinate)
short	w,h;	Size of tile in pixels
} TILE;
Explanation
Draws a flat colored sprite of specified size.
Use setTile to initialize the packet before adding it to an ordering table.
### TILE_1, TILE_8, TILE_16
Fixed size 1 x 1, 8 x 8 and 16 x 16 colored sprites.
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Structure
typedef struct _TILE_1 {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_1;

typedef struct _TILE_8 {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_8;

typedef struct _TILE_16 {
u_long	tag;	Pointer tag to next primitive packet
u_char	r0,g0,b0,code;	RGB color of tile + packet code
short	x0,y0;	Position of tile (top-left coordinates)
} TILE_16;
Explanation
Draws a fixed size 1 x 1, 8 x 8 or 16 x 16 flat colored sprite.
Use setTile1, setTile8, setTile16 to initialize the packet before adding it to an ordering table.
## Functions
### AddPrim
Non macro version of addPrim
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void AddPrim(
u_long *ot,	Pointer to an ordering table element
void *p)	Pointer to a primitive packet
Explanation
Links a primitive packet to an ordering table element by setting the value from the specified table element to the primitive packet’s tag element (with the size byte retained) and the pointer to the packet is set to the specified table element.
It is recommended to generate primitive packets in a global buffer to ensure that they do not get overwritten when the GPU gets around to processing the primitive (ie. If you allocate the primitive as a local variable in a function, it may have been overwritten when the GPU gets to draw it).
A common misconception among many PS1 homebrew programmers is they sometimes believe only a single primitive packet can be added to each ordering table element. This is false because adding another primitive to an ordering table element that already has a primitive concatenates to the chain, not replace the element.
Therefore, an ordering table length of 4 to 8 elements is usually enough for purely 2D projects. Higher ordering table sizes are recommended for projects featuring 3D visuals.
See also
ClearOTagR DrawOTag
### ClearOTagR
Initializes an array to an empty ordering table (reverse order)
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void ClearOTagR(
u_long *ot,	Pointer to an array to initialize into a linked list
int n)	Number of array elements
Explanation
Initializes an array of n elements specified by *ot into a linked list to use as an ordering table. An ordering table consists of an array of pointers that point from one entry to the next which primitives may be added to the chain.
This function uses DMA to clear the ordering table. It prepares a reverse order list which starts at the last entry of the array and ends at the first. This is ideal for 3D graphics as higher table entries are drawn first and lower entries are drawn last. Primitives added to one entry first are always drawn last.
To begin processing of an ordering table array initialized by this function, execute DrawOTag(ot+n-1) (draw from last entry of array) since the ordering table is initialized with pointers in reverse order.
When adding an ordering table to another ordering table using addPrims, specify the last element for p0 and the first element for p1 if the ordering table is cleared by this function.
See Also
AddPrim DrawOTag
### DrawOTag
Executes an ordering table
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void DrawOTag(
u_long *ot)	Pointer to an ordering table array to draw.
Explanation
Draws out or executes primitives linked to the ordering table array specified by *ot.
When drawing an ordering table initialized by ClearOTagR, you must specify the last array element of the ordering table.
DrawOTag uses DMA to send primitives to the GPU at high speed and may be non-blocking during DMA transfer. Use DrawSync to check if the DMA transfer and execution of primitives has completed.
See also
DrawSync ClearOTagR
### DrawPrim
Draws a primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R17	06/07/2021
Syntax
void DrawPrim(
void *pri)	Pointer to a primitive
Explanation
Draws or execute the primitive specified by pri. Uses software I/O to send the primitive to the GPU, so its not recommended for use in drawing a large amount of primitives.
Use only for drawing a few primitives in a very simple single buffered menu for example.
### DrawSync
Waits until all GPU drawing or VRAM transfers have completed
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	12/21/2018
Syntax
int DrawSync(
int mode)	Function mode
Explanation
Waits until the GPU has finished processing drawing commands or VRAM transfers. If mode is non-zero, returns the number of words remaining in a DMA transfer.
Work in progress
This function does not timeout if the GPU locks up due to a bad packet or corrupted ordering table as of version 0.09b.
Returns
Number of words remaining in transfer if mode = 1.
### DrawSyncCallback
Sets a callback function that is executed on drawing or VRAM transfer completion
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R16	07/17/2019
Syntax
void *DrawSyncCallback(
void (*func)())	Pointer to a function
Explanation
Sets a callback function specified by func which will be executed on every drawing completion or VRAM transfer. Setting 0 will disable the callback.
Because the callback function is executed inside an interrupt handler, it is necessary to finish any processing as soon as possible. Sub function calls should be kept a minimum as the stack in the ISR is limited.
It is not recommended to issue VRAM or OT transfer operations within the callback function, use it only to set variables for keeping track of drawing and transfer completions.
It is recommended to define any variable manipulated by a callback function as volatile, to make sure any code reading the value will always receive changes.
See also
DrawSync
### GetTimInfo
Get image parameters of a TIM image file
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	R1	02/02/2019
Syntax
int GetTimInfo(
unsigned int *tim,	Pointer to a TIM image file
TIM_IMAGE *timimg)	Pointer to a TIM_IMAGE structure
Explanation
Retrieves parameters from a TIM file and stores relevant values to a TIM_IMAGE structure.
Return value
0: success, 1: invalid file ID, 2: unsupported TIM version
See also
TIM_IMAGE
### GetVideoMode
Gets the current video standard mode
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
int GetVideoMode()
Explanation
Returns the current video standard mode.
Differences
Unlike the official libraries, this function returns the current video mode standard (ie. If this function is called on a PAL machine while in a PAL display mode, it returns 1 or MODE_PAL).
Returns
MODE_NTSC = NTSC
MODE_PAL = PAL
See also
SetVideoMode
### LoadImage
Upload image data to VRAM
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void LoadImage(
RECT *rect,	Pointer to a RECT specifying VRAM destination coordinates
unsigned int *data)	Pointer to source image data
Explanation
Uploads image data from the source address data to VRAM. The image size and destination offset in VRAM is specified by rect using a RECT object.
LoadImage uses DMA to upload data to VRAM at high speed and may be non-blocking. Use DrawSync to check if DMA transfer has completed. Using DrawSync when uploading multiple images at once is not necessary as LoadImage will wait for a previous transfer to complete before uploading.
If you want to upload a texture image on every frame in a real time sequence it is best to perform the upload after a DrawSync call.
See also
DrawSync GetTimInfo
### PutDrawEnv
Applies a DRAWENV structure
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void PutDrawEnv(
DRAWENV *draw)	Pointer to a DRAWENV structure
Explanation
Applies the specified DRAWENV structure to the GPU. This function is best called when the GPU is not busy processing any primitives. Use the DrawSync function to wait for the GPU to complete any drawing operations.
Alternatively a DR_ENV struct can be used to change the drawing environment mid-drawing (ie. for split screen rendering).
See also
DRAWENV

### PutDispEnv
Applies a DISPENV structure
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void PutDispEnv(
DISPENV *disp)	Pointer to a DISPENV structure
Explanation
Applies the specified DISPENV struct to the GPU. This function is best called immediately when a V-Blank occurs (using VSync) for updating the screen regularly. Use the VSync function to wait until a V-Blank occurs.
See also
DISPENV VSync
### ResetGraph
Resets the graphics subsystem
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void ResetGraph(
int mode)	Reset mode
Explanation
Resets the GPU and graphics subsystem of libpsxgpu according to mode.
On first call, this function will additionally hook the ISR subroutine to the kernel, hooks the internal VSync callback, uninstall the BIOS CD subsystem and exit critical section regardless of mode. Because of this, it is highly recommended to call this function at the beginning of your program even if you don’t plan to do any graphics.
The following describes the behavior of the available mode numbers. The exact behavior in the official SDK is not known yet.
Mode	Operation
0	Resets the GPU entirely including video mode (default of 256x240) and sets	display mask to 0.
1	Cancels any ongoing DMA transfer and resets the GPU command buffer.
3	Resets the GPU command buffer.

### SetDefDispEnv
Sets a display environment with default parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/08/2019
Syntax
SetDefDispEnv(
DISPENV *disp,	Pointer to a DISPENV structure
int x, int y,	X, Y framebuffer coordinates to display
int w, int h)	Display resolution
Explanation
Prepares a DISPENV structure with the specified framebuffer and resolution coordinates using default video parameters.
The defaults are the screen element of DISPENV is set to zeroes, isinter is set 0 and isrgb24 is set 0.
See also
DISPENV PutDispEnv
### SetDefDrawEnv
Sets a drawing environment with default parameters
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/08/2019
Syntax
SetDefDrawEnv(
DRAWENV *disp,	Pointer to a DRAWENV structure
int x, int y,	X, Y framebuffer coordinates to draw to
int w, int h)	Draw area size
Explanation
Prepares a DRAWENV structure with the specified framebuffer and resolution coordinates using default parameters.
The ofs[] elements of DRAWENV is set 0 (top-left), tw is set 0 (default texture window settings), tpage to 0x0a (640, 0), dtd to 1 (dithering enabled), dfe to 0 (don’t draw to displayed area), isbg to 0 (no draw area clear) and clear color values set to 0.
See also
DRAWENV PutDrawEnv
### SetDispMask
Sets the display mask
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/08/2019
Syntax
void SetDispMask(
int mask)	Display mask setting (0: no display, 1: display)
Explanation
Sets the display mask of the GPU. If mask is 0, the console will only show a black screen but sync signals are still sent to the television.
This function is useful for hiding garbage shown during video init/setup. ResetGraph automatically sets the display mask to 0.
Best called after VSync and PutDispEnv.
### SetVideoMode
Sets the video standard
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2021
Syntax
void SetVideoMode(
int mode)	Video standard to set
Explanation
Sets the video standard by mode (MODE_NTSC for NTSC or MODE_PAL for PAL), normally used to override the current video standard of the console.
Keep in mind that using a video standard other than what is designated on the console itself to color problems or unstable picture without modifications to the hardware. On earlier models the picture will go out and vertical retrace interrupts stop, causing the system to lock up.
### StoreImage
Download image data from VRAM
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R21	06/07/2021
Syntax
void StoreImage(
RECT *rect,	Pointer to a RECT specifying VRAM source coordinates
u_long *data)	Pointer to store downloaded image data
Explanation
Downloads a portion of VRAM from an area specified by rect, and stores the downloaded pixel data to a buffer specified by data.
StoreImage uses DMA to upload data to VRAM at high speed and could be non-blocking, use DrawSync to ensure the DMA transfer has completed.
See also
DrawSync
### VSync
Wait for vertical retrace, return hblank count since last call or elapsed vertical blank counter
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/23/2019
Syntax
void VSync(
int mode)	Mode
Explanation
Waits until a vertical retrace occurs or returns a value using the method specified by mode, as defined below.
Mode	Operation
0	Waits until a vertical retrace event occurs.
1	Only return the Hblank count elapsed since last VSync call.
n>1	Waits until n vertical retrace events occur.
n<0	Returns number of vertical retrace events elapsed since the beginning of the	program.
VSync() will timeout if the vertical blanking interrupt stops working either due to calling ChangeClearPAD(1), or calling _InitPad() without calling ChangeClearPAD(0) next. The function will attempt to restart vertical blanking interrupts by calling ChangeClearPAD(0) and ChangeClearRCnt(3, 0).
VSync() may also timeout if a large wait value is specified. Use a for-loop that calls VSync(0) instead to get around this limitation.
Return value
Return value varies depending on the value specified by mode.
Mode	Return value
>=0	Hblank count elapsed since last VSync call.
<0	Number of vertical retrace events elapsed since the start of your program.
See also
VSyncCallback
### VSyncCallback
Sets a specified function to be executed on every V-blank
Library	Header	Original	Introduced	Documentation Date
liblibpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
void *VsyncCallback(
void (*func)())	Pointer to a callback function
Explanation
Sets a callback function specified by func called on every V-blank. Setting 0 will disable the callback.
Because the callback function is executed during a critical section inside an ISR, it is necessary to finish any processing quickly. Sub function calls should also be kept at minimum as the stack in the ISR is limited.
It is recommended to define any variable manipulated by a callback function as volatile to make sure that any loop reading the value will always read the variable for changes.
Returns
Pointer to last callback function set.
See also
VSync
## Macros
### addPrim
Links a primitive packet to an ordering table
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
addPrim(
ot,	Pointer to an ordering table element
p)	Pointer to a primitive packet
Explanation
Links a primitive packet to an ordering table element by setting the value from the specified table element to the primitive packet’s tag element (with the size byte retained) and the pointer to the packet is set to the specified table element.
It is recommended to generate primitive packets in a global buffer to ensure that they do not get overwritten when the GPU gets around to processing the primitive (ie. If you allocate the primitive as a local variable in a function, it may have been overwritten when the GPU gets to draw it).
A common misconception among PS1 homebrew programmers is that they sometimes believe that only a single primitive packet can only be added to each ordering table element. This is false as adding another primitive to an ordering table element that already has a primitive added to it will only add to the chain, not replace it so pretty much any number of primitives can be added to a single table element. Therefore, an ordering table length of 4 to 8 elements is usually enough for a 2D game project.
See also
ClearOTagR DrawOTag
### addPrims
Links an ordering table to another ordering table
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
addPrims(
ot,	Pointer to an ordering table element
p0,	Pointer to the first element of the ordering table to add
p1)	Pointer to the last element of the ordering table to addition
Explanation
This macro links one ordering table specified by p0 and p1 to another ordering table.
The ordering table element that is considered the first element in the chain depends on which function was used to prepare the ordering table. If the ordering table was cleared using ClearOTagR the last element of the array is the first and the first element is the last, if the ordering table is cleared using ClearOTag the first element in the array is the first and the last element is the last.
See also
ClearOTagR
### getClut
Calculates and returns a CLUT value
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
getClut(
x, y)	Framebuffer coordinates to a CLUT
Explanation
Calculates a CLUT value from the specified coordinates. The resulting value is used on textured primitives with a CLUT field. x must be a multiple of 16 units, the value will be rounded down to the nearest lower multiple otherwise.
A CLUT is needed only if the texture color depth is 4-bit or 8-bit.
Primitives with a CLUT field include SPRT, SPRT_8, SPRT_16, POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
### getTPage
Calculates and returns a texture page value
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/16/2019
Syntax
getTPage(
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Blend operator mode (see below)
x, y)	Framebuffer coordinate of texture page
Explanation
Calculates a texture page value using the specified coordinates. The resulting value is used with textured primitives that have a Tpage field or a DR_TPAGE primitive (using setDrawTPageVal).
The framebuffer coordinates should be a multiple of 64 for the X axis and a multiple of 256 for the Y axis, the coordinates will be rounded down to the nearest lower multiple otherwise.
The following lists the blend modes for semi-transparent primitives (abr):
Mode	Operation
0	B:50%	+	F:50%	(50% alpha)
1	B:100%	+	F:100%	(additive)
2	B:100%	-	F:100%	(subtractive)
3	B:100%	-	F:25%	(subtract 25%)
Primitives that have a Tpage field include POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4, use DR_TPAGE and setDrawTPage or setDrawTPageVal for textured primitives without a Tpage field.
Returns
16-bit texture page value.
See also
setDrawTPage setDrawTPageVal
### setClut
Sets the CLUT field of a primitive by coordinates
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
setClut(
p,	Pointer to a primitive struct with a CLUT field
x, y)	Framebuffer coordinates to a CLUT
Explanation
Sets the CLUT field of a primitive by framebuffer coordinates. x must be a multiple of 16 pixels, the value will be rounded down to the nearest lower multiple otherwise.
Primitives with a CLUT field include SPRT, SPRT_8, SPRT_16, POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
See also
getClut
### setDrawArea
Initializes a DR_AREA primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	R32	01/14/2022
Syntax
setDrawArea(
p,	Pointer to a DR_AREA primitive
r)	Pointer to a RECT structure
Explanation
Initializes a DR_AREA primitive p and sets the drawing area coordinates of the primitive from r. The drawing area coordinates are VRAM absolute and can be used to perform graphics clipping or off-screen rendering mid-drawing (ie. procedural textures).
When changing the drawing area, the drawing offset may also need to be changed with a DR_OFFSET packet.
Once the primitive is initialized it can be registered to an ordering table using addPrim.
See Also
addPrim
### setDrawOffset
Initializes a DR_OFFSET primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	R32	01/14/2022
Syntax
setDrawOffset(
p,	Pointer to DR_OFFSET primitive
_x,	X coordinate of new drawing offset
_y)	Y coordinate of new drawing offset
Explanation
Initializes a DR_OFFSET primitive p and sets the drawing offset coordinates from _x and _y. This sets the home coordinates (0,0) for drawing primitives and the offset itself is VRAM absolute, completely independent from the current drawing area.
For 3D graphics it is generally preferred to use GTE offsets rather than the drawing offset in most situations.
Once the primitive is initialized it can be registered to an ordering table using addPrim.
See Also
addPrim
### setDrawMask
Prepares a DR_MASK primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	Yes	R1	07/17/2019
Syntax
setDrawMask(
p,	Pointer to a DR_MASK primitive
sb,	Set mask bit on pixels drawn (0: don’t set, 1: set)
mt)	Mask test (0: draw always, 1: don’t draw on masked pixels)
Explanation
Prepares and sets the specified values to a DR_MASK primitive. The mask feature allows for limited stencil effects with the GPU.
Setting sb to 1 makes primitives set the mask bit on every pixel drawn, the mask bit is stored on the 16th bit of each pixel within the drawing area. The mask is cleared by primitives if sb is set 0.
Textured primitives with semi-transparency bits set on either the pixels or CLUT colors of the texture will also set this mask bit regardless of the sb setting. Setting mt to 1 enables mask test, which prohibits drawing on areas that have the mask bit set in the drawing area.
The mask settings affects all GPU drawing packets as well as GPU VRAM transfer and move operations, it is recommended to issue a DR_MASK with sb:0 and mt:0 to reset the mask settings after performing mask effects.
### setDrawTPage
Prepares a DR_TPAGE primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/16/2019
Syntax
setDrawTPage(
p,	Pointer to a DR_TPAGE primitive
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Blend operator mode (see getTPage)
x, y)	Framebuffer coordinate of texture page
Explanation
Prepares and sets the specified values to a DR_TPAGE primitive, used to change the current Tpage of the GPU mid-drawing for primitives that do not have a Tpage field, and/or to set a blending operator for semi-transparent, non-textured primitives.
The framebuffer coordinates should usually be a multiple of 64 for the X axis and a multiple of 256 for the Y axis, the coordinates will be rounded down to the nearest lower value otherwise. Texture color depth has no effect on framebuffer coordinates.
See also
DR_TPAGE
### setLineF2
Prepares a LINE_F2 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R23	07/16/2019
Syntax
setLineF2(
p)	Pointer to a LINE_F2 primitive
Explanation
Prepares a LINE_F2 packet by setting the appropriate packet size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineF3
Prepares a LINE_F3 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R23	07/16/2019
Syntax
setLineF3(
p)	Pointer to a LINE_F3 primitive
Explanation
Prepares a LINE_F4 packet by setting the appropriate packet size and code values to the primitive, and sets a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineF4
Prepares a LINE_F4 primitives
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setLineF4(
p)	Pointer to a LINE_F4 primitive
Explanation
Prepares a LINE_F4 packet by setting the appropriate packet size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_F2, LINE_F3, LINE_F4
### setLineG2
Prepares a LINE_G2 primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setLineG2(
p)	Pointer to a LINE_G2 primitive
Explanation
Prepares a LINE_G2 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setLineG3
Prepares a LINE_G3 primitive
Library	Header File	Original	Introduced	Documentation Date
libpsxgpu.a	psxgpu.h	No	R23	06/07/2019
Syntax
setLineG3(
p)	Pointer to a LINE_G3 primitive
Explanation
Prepares a LINE_G3 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setLineG4
Prepares a LINE_G4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/16/2019
Syntax
setLineG4(
p)	Pointer to a LINE_G4 primitive
Explanation
Prepares a LINE_G4 packet by setting the appropriate size and code values to the primitive, and adds a terminator word at the end of the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
LINE_G2, LINE_G3, LINE_G4
### setPolyF3
Prepares a POLY_F3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyF3(
p)	Pointer to a POLY_F3 primitive
Explanation
Prepares a POLY_F3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_F3, POLY_F4
### setPolyFT3
Prepares a POLY_FT3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyFT3(
p)	Pointer to a POLY_FT3 packet
Explanation
Prepares a POLY_FT3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_FT3, POLY_FT4
### setPolyG3
Prepares a POLY_G3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyG3(
p)	Pointer to a POLY_G3 packet
Explanation
Prepares a POLY_G3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_G3, POLY_G4
### setPolyGT3
Prepares a POLY_GT3 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyGT3(
p)	Pointer to a POLY_G3 packet
Explanation
Prepares a POLY_GT3 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_GT3, POLY_GT4
### setPolyF4
Prepares a POLY_F4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyF4(
p)	Pointer to a POLY_F4 packet
Explanation
Prepares a POLY_F4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_F3, POLY_F4
### setPolyFT4
Prepares a POLY_FT4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyFT4(
p)	Pointer to a POLY_FT4 packet
Explanation
Prepares a POLY_FT4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_FT3, POLY_FT4
### setPolyG4
Prepares a POLY_G4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyG4(
p)	Pointer to a POLY_G4 packet
Explanation
Prepares a POLY_G4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_G3, POLY_G4
### setPolyGT4
Prepares a POLY_GT4 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setPolyGT4(
p)	Pointer to a POLY_GT4 packet
Explanation
Prepares a POLY_GT4 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, tpage, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
POLY_GT3, POLY_GT4
### setRECT
Sets coordinates to a RECT struct
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
setRECT(
v,	Pointer to a RECT struct
_x,	X coordinate to set
_y,	Y coordinate to set
_w,	Width coordinate to set
_h)	Height coordinate to set
Explanation
Sets the x, y, w, and h fields of a RECT specified by v, with coordinates specified by _x, _y, _w and _h. Cleaner looking to use over setting the fields directly.
See also
RECT
### setSprt
Prepares a SPRT primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setSprt(
p)	Pointer to a SPRT packet
Explanation
Prepares a SPRT packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y, coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT
### setSprt8
Prepares a SPRT_8 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setSprt8(
p)	Pointer to a SPRT_8 packet
Explanation
Prepares a SPRT_8 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT_8, SPRT_16
### setSprt16
Prepares a SPRT primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setSprt16(
p)	Pointer to a SPRT_16 packet
Explanation
Prepares a SPRT_16 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates, clut and color) to the primitive and before adding it to an ordering table using addPrim.
See also
SPRT_8, SPRT_16
### setTexWindow
Prepares a DR_TWIN primitive
Library	Header File	Original	Introduced	Date Documented
none	psxgpu.h	No	R34	10/22/2019
Syntax
setTexWindow(
p,	Pointer to a DR_TWIN structure
r)	Pointer to a RECT structure
Explanation
Prepares a DR_TWIN primitive by setting the packet size and packet code based on arguments specified.
The (x, y) coordinates in the RECT structure specifies the offset of the texture window in units of 8 pixels (1 = 8 pixels). The offset adds to the (u,v) coordinates of any textured primitive.
The (w, h) coordinates specifies the texture window constraint in units of 8 pixels (1 = 8 pixels). The constraint limits the range of pixels that can be read, and wraps pixels when texture coordinates exceed the size of the constraint.
### setTile
Prepares a TILE primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setTile(
p)	Pointer to a TILE packet
Explanation
Prepares a TILE packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE
### setTile1
Prepares a TILE_1 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setTile(
p)	Pointer to a TILE_1 packet
Explanation
Prepares a TILE_1 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_1, TILE_8, TILE_16
### setTile8
Prepares a TILE_8 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setTile8(
p)	Pointer to a TILE_8 packet
Explanation
Prepares a TILE_8 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_1, TILE_8, TILE_16
### setTile16
Prepares a TILE_16 primitive
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	06/07/2019
Syntax
setTile16(
p)	Pointer to a TILE_16 packet
Explanation
Prepares a TILE_16 packet by setting the appropriate size and code values to the primitive.
Use this macro before setting other values (x,y coordinates and color) to the primitive and before adding it to an ordering table using addPrim.
See also
TILE_1, TILE_8, TILE_16
### setTPage
Sets the Tpage of a primitive by coordinates
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
setTPage(
p,	Pointer to a primitive with a Tpage field
tp,	Texture color depth (0: 4-bit, 1: 8-bit, 2: 16-bit)
abr,	Semi-transparency blend operator (see getTPage)
x, y)	Framebuffer coordinates to a texture page
Explanation
Sets the Tpage field of a primitive by coordinates.
Primitives that have a Tpage field include POLY_FT3, POLY_FT4 and POLY_GT3, POLY_GT4.
See also
getTPage
### setVector
Sets coordinates to a VECTOR or SVECTOR struct
Library	Header File	Original	Introduced	Date Documented
libpsxgpu.a	psxgpu.h	No	R1	07/17/2019
Syntax
setVector(
v,	Pointer to a VECTOR or SVECTOR struct
_x,	X coordinate to set
_y,	Y coordinate to set
_z)	Z coordinate to set
Explanation
Sets the vx, vy and vz fields of a VECTOR or SVECTOR struct specified by v, with coordinates specified by _vx, _vy and _vz. Cleaner looking to use over setting the fields directly.
# Miscellaneous Library

## Overview
The miscellaneous library provides functions mostly to aid in prototyping and testing.
## Functions
### DMACallback
Sets a callback routine for a DMA interrupt
Library	Header File	Original	Introduced	Date Documented
libpsxetc.a	psxgpu.h	Yes	R16	07/16/2019
Syntax
void *DMACallback(
int dma,	DMA channel to set callback
void (*func)())	Callback function
Explanation
Sets a callback function specified by func to a DMA channel specified by dma, executed whenever a DMA transfer for the specified channel finishes. Calling this function will automatically install a handler on IRQ3 using InterruptCallback to handle DMA interrupts.
This function is not normally exposed to programmers in the official SDK, but is made available in LibPSn00b for low-level prototyping and advanced programmers. Use this function only if you know exactly what you're going to do with it.
The following lists the hardware device associated with each DMA channel, channels used by libraries should not be used to avoid conflicts:
Channel	Device
0	MDEC input
1	MDEC output
2	GPU (used by libpsxgpu)
3	CD-ROM (used by libpsxcd)
4	SPU
5	PIO
6	OTC (used by libpsxgpu)
Setting a DMA callback automatically adds an interrupt callback handler on IRQ3 using InterruptCallback(). If a callback routine on IRQ3 has been previously set, DMACallback will not set its own handler.
The callback is never an interrupt handler and a callback function must be written as a normal function. Since the callback function is called within an exception handler, the function must return as soon as possible. Recursive function calls must be kept a minimum due to limited stack in the ISR subsystem. DMA interrupt status bits are automatically acknowledged on return so the callback routine does not need to acknowledge it manually.
To uninstall a callback routine, simply specify NULL or 0 for func. It will also remove the IRQ enable bit of the corresponding DMA channel. If all DMA callbacks have been removed, the DMA callback handler is removed from the ISR subsystem.
Returns
Pointer to the last installed callback routine.
### FntLoad
Upload debug font texture to VRAM
Library	Header File	Original	Introduced	Documentation Date
libpsxetc.a	psxetc.h	No	R1	09/25/2019
Syntax
void FntLoad(
int x, int y)	Framebuffer coordinates to upload font texture
Explanation
Uploads the font texture to VRAM, so debug text drawing functions can be used. This function must be called first before using FntOpen(), FntPrint() and FntFlush().
The size of the font texture is 32x64 plus a 16 color CLUT immediately below the texture. The X coordinate must be a multiple of 64 and the Y coordinate a multiple of 256.
This function can also close all text streams previously created by FntOpen().
See also
FntOpen
### FntOpen
Opens a debug font text stream
Library	Header File	Original	Introduced	Documentation Date
libpsxetc.a	psxetc.h	No	R28	09/25/2019
Syntax
int FntOpen(
int x, int y,	X,Y coordinate of text window
int w, int h,	Width and height of text window
int isbg,	Draw background (0: none, 1: black, 2: semi-transparent black)
int n)	Number of characters to allocate
Explanation
Opens a text stream window using the debug font uploaded by FntLoad().
The text will only draw inside the area specified by (x,y)-(w,h), to allow you to crete multiple text streams at different portions of the screen. The text will wrap if it passes the size of the specified window area. The coordinates are draw area relative and not framebuffer absolute, so you don’t have to adjust it relative to your current draw area coordinates.
Isbg specifies if a solid background should be drawn below the text to improve text readability. Specifying 1 draws a solid black rectangle as the text background, while a value of 2 draws a semi-transparent black rectangle, which not only improves text readability but also allow graphics behind the window to be visible.
n specifies how many characters to allocate for the text stream.
Up to 8 text streams can be created at once. Previously opened streams can be closed and deallocated using FntLoad.
Returns
Number of text stream opened, -1 if no more streams can be opened.
See also
FntLoad FntPrint
### FntPrint
Print text to specified text stream
Library	Header File	Original	Introduced	Documentation Date
libpsxetc.a	psxetc.h	No	R28	09/25/2019
Syntax
int FntPrint(
int id,	Stream number (-1 = use last opened stream)
const char *fmt,	Format string (same syntax as printf())
… )	Text format arguments
Explanation
Prints text to the specified text stream created by FntOpen.
This function works much like fprintf(), but text output is directed to the debug font text stream. Id specifies which text stream created by FntOpen to print the text to, or specify -1 to write the text to the last opened stream.
Because of modern GCC requiring at least one named argument in function names, this function does not have the same syntax as FntPrint in the official SDK, and a stream number must be specified at all times.
Use FntFlush to draw the text written in the specified text stream.
Returns
Number of characters written.
See also
FntLoad FntOpen FntFlush
### FntFlush
Draws a text stream
Library	Header File	Original	Introduced	Documentation Date
libpsxetc.a	psxetc.h	No	R28	09/25/2019
Syntax
char *FntFlush(
int id)	Stream number (-1 = use last opened stream)
Explanation
Draws the text window and characters of the specified text stream.
The function waits for drawing to complete, then draws the primitives using DMA transfer and finally waits for it to complete. This helps ensure the text primitives are fully drawn, though it may result to some performance loss.
Returns
Pointer to an internal primitive buffer used to draw the text stream, can be drawn using DrawOTag.
See also
FntLoad FntOpen FntPrint
### GetInterruptCallback
Returns the address of the callback function of a specified interrupt
Library	Header File	Original	Introduced	Documentation Date
libpsxetc.a	psxgpu.h	Yes	R16	06/19/2019
Syntax
void *GetInterruptCallback(
int irq)	Interrupt number
Explanation
Gets the address of the callback function of an interrupt.
Returns
Pointer to the callback function last set.
See also
InterruptCallback
### InterruptCallback
Sets a callback routine for an interrupt
Library	Header File	Original	Introduced	Date Documented
libpsxetc.a	psxgpu.h	Yes	R15	07/16/2019
Syntax
void *InterruptCallback(
int irq,	Interrupt number to install callback
void (*func)())	Callback function
Explanation
Sets a callback function specified by func to the ISR, which is executed whenever an interrupt specified by irq occurs. Only one callback routine can be set per interrupt number at a time.
This is a special low-level function that is not normally used by programmers in the official SDK and is normally only called internally by the libraries. It is exposed in LibPSn00b for better control over the hardware for more advanced programmers. Use this function only if you know exactly what you’re doing.
The following lists the hardware device associated with each interrupt number:
Interrupt	Device
0	Vsync (used by libpsxgpu)
1	GPU (triggered only by a special GPU packet)
2	CD-ROM (used by libpsxcd)
3	DMA (used by libpsxgpu and libpsxcd)
4	Timer 0
5	Timer 1
6	Timer 2
7	Pad & Memory card
8	Serial (used by libpsxsio)
9	SPU
10	Light-gun & Expansion port
Most hardware devices would only generate an interrupt when enabled by their I/O port registers.
This function should only be called while in critical section. The ISR automatically acknowledges interrupts so the callback routine does not need to acknowledge it (except hardware devices that additionally need to be acknowledged by their I/O registers). Avoid calling too many sub functions in the callback routine as the size of the stack in the ISR is limited.
To uninstall a callback routine, simply specify NULL or 0 for func. It will also remove the IRQ mask bit of the corresponding interrupt in I_MASK which disables the interrupt.
Returns
Pointer to the last installed callback routine.
See Also
DMACallback
# Serial Input/Output Library

## Overview
The serial library provides functions to configure and control the serial interface of the PSX. It also provides a custom device intended to replace the default tty device to direct tty output from printf() calls to the serial interface, to be viewed in a serial terminal.
The PSX’s serial interface is capable of baud rates of up to 1Mbaud but 230400 baud is the highest data rate that USB serial adapters (such as a CH340) can receive. Achieving reliable communications with high data rates is yet to be studied further.
### Library Status
As of September 12, 2020, the state of the LibPSn00b SIO library is as follows:
Feature	Status
Interface Init	Fully working
Data transmit/receive	Fully working
SIO TTY driver	Fully working
Handshake/Flow Control	Fully working
Interrupts	Fully working
## Functions
### _sio_control
Serial control function
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	R15	07/16/2019
Syntax
int _sio_control(
int cmd,	Command
int arg,	Subcommand
int param)	Parameter
Explanation
Multi-purpose serial control function, used to control and retrieve every aspect of the serial interface.
The behavior of this function varies depending on the values specified by cmd and arg.
The following describes command/argument combinations:
cmd	arg	Function
0	0	Read serial status register.
0	1	Read serial control register.
0	2	Read serial mode register.
0	3	Read serial baud rate.
0	4	Read 1 byte from serial interface (returns byte	received).
1	1	Set serial control register.
1	2	Set serial mode (parameters specified by param).
1	3	Set serial baud rate (value specified by param).
1	4	Write 1 byte to serial interface (byte value specified by	param).
2	0	Reset serial interface.
2	1	Acknowledge serial interrupt and comms errors.

The following describes serial control options (some values not documented in official SDK):
Bits	Definition	Description
0	CR_TXEN	TX enable.
1	CR_DTR	Output DTR signal.
2	CR_RXEN	RX enable.
3	CR_BRK	Invert TX logic levels.
4	CR_INTRST	Acknowledge IRQ and comms errors.
5	CR_RTS	Output RTS signal.
6	CR_ERRRST	Reset serial hardware.
7	Unknown (always 0).
8-9	Interrupt when RX buffer has n bytes.
CR_BUFSIZ_1	00: Interrupt on 1 byte.
CR_BUFSIZ_2	01: Interrupt on 2 bytes.
CR_BUFSIZ_4	10: Interrupt on 4 bytes.
CR_BUFSIZ_8	11: Interrupt on 8 bytes.
10	CR_TXIEN	Interrupt on TX ready.
11	CR_RXIEN	Interrupt on RX receive.
12	CR_DSRIEN	Interrupt on DSR signal.
13-15	Unused (always zero).
The following describes serial mode options:
Bits	Definition	Description
0-1	None	Baud rate reload factor (must be 0x2 always).
2-3	Character length.
MR_CHLEN_5	00: 5 bits per word.
MR_CHLEN_6	01: 6 bits per word.
MR_CHLEN_7	10: 7 bits per word.
MR_CHLEN_8	11: 8 bits per word.
4	MR_PEN	Parity enable.
5	MR_P_EVEN	Odd parity (definition is misleading).
6-7	Stop bit length.
MR_SB_01	01: 1 stop bit.
MR_SB_10	10: 1.5 stop bits.
MR_SB_11	11: 2 stop bits.
8-15	Unused (always zero).
The following describes serial status bits:
Bits	Definition	Description
0	SR_TXRDY	TX ready.
1	SR_RXRDY	Bytes pending in RX buffer.
2	SR_TXU	TX completed.
3	SR_PERROR	Parity error.
4	SR_OE	RX buffer overflow.
5	SE_FE	RX bad stop bit.
6	RX input level.
7	SR_DSR	DSR signal level.
8	SR_CTS	CTS signal level.
9	SR_IRQ	Interrupt request.
10	Unknown (always zero).
11-25	15-bit baud rate timer.
### AddSIO
Installs a serial tty device
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	R15	06/14/2019
Syntax
void AddSIO(
int baud)	Baud rate.
Explanation
Replaces the default BIOS tty device (and Caetla’s tty device) with a serial tty device which redirects all stdout output (such as printf) to serial. The data rate is specified by baud, the rest of the parameters are 8 data bits, 1 stop bit, no parity and no hardware handshake by default.
This function can be called at the very beginning of your program (even before ResetGraph) to receive every printf message in your program.
### DelSIO
Deletes the serial tty device
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	R15	06/14/2019
Syntax
void DelSIO(void)
Explanation
Deletes the serial tty device, not recommended as any further tty output will likely crash the system.
### WaitSIO
Waits for serial
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	Yes	R15	06/14/2019
Syntax
void WaitSIO(void)
Explanation
Waits until a single byte is received from the serial interface, intended to be called immediately after AddSIO and is useful for pausing your program so you can open a terminal program and receive all tty messages.
### Sio1Callback
Sets a serial callback routine
Library	Header File	Original	Introduced	Date Documented
libpsxsio.a	psxsio.h	No	R15	06/14/2019
Syntax
void *Sio1Callback(
void (*func)(void))	Callback function.
Explanation
Sets a function specified by func as a callback routine that is executed whenever the serial interface generates an interrupt enabled by CR_TXIEN, CR_RXIEN or CR_DSRIEN using _sio_control(1, 1, <param>). If func is zero, the callback is disabled.
It is recommended to read at least 1 byte from the serial interface and call _sio_control(2, 1, 0) to acknowledge the serial interrupt at the end of your callback routine.
Since the callback function is executed in the global ISR, sub function calls must be kept at minimum due to limited stack available. The callback function must return as soon as possible to avoid missing any further interrupt requests.
Return value
Address of previously set callback function.
# Reference Manual Changelog
March 25, 2022:
- Updated documentation for CdGetSector() to correspond with changes implemented to this function since 2021-12-23.
- Corrected description of CdReadCallback() function.
January 14, 2022:
- Removed documentation for SetDrawTPageVal() function.
- Documented primitives DR_AREA, DR_OFFSET, DR_TWIN
- Documented macros setDrawArea, setDrawOffset
June 6, 2021:
Updated psxgpu and psxcd types to account for library changes.
December 3, 2020:
Documented several important functions of the Geometry Library.
December 2, 2020:
Moved InterruptCallback(), DMACallback() and GetInterruptCallback() to Miscellaneous Library chapter, as well as corrected the Original status of the aforementioned functions (technically, they aren’t original, but the official libraries do not expose it to programmers).
September 18, 2020:
Document recreated from Revision 60 of document to fix broken formatting spread across entire document.